PROPOSAL

Antietam Fire Apparatus, Inc. is pleased to offer the proposed vehicle to meet the intent of the fire department specifications.  KME Fire Apparatus is a leading manufacturer in custom and commercial fire fighting vehicles.

Questions or concerns pertaining to this proposal can be answered by contacting the following KME representative:

Bill White

Antietam Fire Apparatus

19932 Beaver Creek Road

Hagerstown, MD  21740

Phone:	(877) 378-2781 / (301) 797-1410

Cell:	(443) 336-6688

Fax:	(301) 797-1412

Email: 	bwhite@antietamfireapparatus.com

KME-KOVATCH ORGANIZATION HISTORY

The KME-Kovatch Organization brings to the fire and specialty vehicle market over six decades of broad-based experience in vehicle manufacturing, sales and service.  The company was founded in 1946 and today is still a family owned enterprise with a history of consistent growth, profitability and success.

In the mid 1960’s, Kovatch began a string of awards from various branches of the United States military.  By the 1970’s, the company had a string of successful rebuild and new manufacture contracts for various branches of the Defense Department.  To this day, Kovatch is known as a premier supplier of specialty apparatus to the Federal government and is a currently working on several contracts.

In the mid 1980’s, Kovatch expanded its products to include a commercial fire apparatus division, now known as KME Fire Apparatus.  By combining decades of specialty vehicle experience with the acquisitions of other manufacturers, KME offers unparalleled products and services.  Today, the Organization manufacturers hundreds of vehicles per year for municipal, industrial, aviation and volunteer fire and rescue service providers.  Our apparatus can be found across the country and increasingly around the world.

The Kme-Kovatch headquarters complex consists of over one-half million square feet and is a totally integrated manufacturing campus for emergency and specialty vehicles.  The facilities include a state of the art fabrication, machining, welding, painting and finishing departments.  We also have a technical manual publication department for our vast line of products.  Our knowledgeable workforce, including marketing, engineering, and manufacturing personnel, work as a team to provide world-class quality.  Other factory locations include California, New York, Oregon and Virginia.

KME has a national distribution network in place for sales and service of fire apparatus, as well as international representatives.  These locations working closely with our factory locations provide a wide range of support including service, maintenance, training and parts.

Quality is very important to our organization.  There is an in-house Quality-Assurance department that is monitored by the Defense Contract Management Command (DCMC)  KME-Kovatch also has UL inspectors on site.  For out of house testing, we utilize the US Army’s facility at Aberdeen Proving ground as well as private testing agencies.

As a true sole source manufacturer, the KME-Kovatch Organization offers a broad line of truly custom apparatus.  KME custom manufacturers its own cabs, chassis, tanks, bodies and aerial devices.  KME products are known worldwide for their quality and reliability.  The line includes a full line of fire apparatus (AARF, aerial, pumper, wild land, rescue, tanker and industrial foam), specialty response vehicles including those for law enforcement, as well as a wide range of fuel and refueling vehicles.

GENERAL INFORMATION

The proposed apparatus will be constructed to withstand the severe and continuous use encountered during emergency fire fighting services.  The apparatus shall be of the latest type, carefully designed and constructed with due consideration to the nature and distribution of the load to be sustained.

These specifications detail the proposal for general design criteria of cab and chassis components, aerial device (if applicable), fire pump and related components (if applicable), water tank (if applicable), fire body, electrical components, painting, and equipment.

All items of these proposal specifications will conform to the National Fire Protection Association Pamphlet No. 1901, latest edition.

KME will furnish satisfactory evidence of our ability to construct, supply service parts and technical assistance for the apparatus specified.

"TOP OF THE LINE" CHASSIS

KME is proposing a custom built chassis, which is "Top Of The Line" including the cab structure and design, electrical system, drive train and frame assembly.

GENERAL CONSTRUCTION

The proposed apparatus, assemblies, subassemblies, component parts, etc., will be designed and constructed with the due consideration to the nature and distribution of the load to be sustained and to the general character of the service to which the apparatus is subjected to when placed in service.  All parts of the apparatus will be designed with a factor of safety, which is equal to or greater than that which is considered standard and acceptable for this class of equipment in fire fighting service.  All parts of the proposed apparatus will be strong enough to withstand general service under full load.  The apparatus will  be so designed that the various parts and readily accessible for lubrication, inspection, adjustment and repair.

The apparatus will be designed and constructed, and the equipment so mounted, with due consideration to distribution of the load between front and rear axles that all specified equipment, including a full complement of specified ground ladders, full water tank, loose equipment, and firefighters will be carried without overloading or injuring the apparatus.

The aerial ladder will be designed as a modular component of the apparatus.  The aerial ladder, its support structure, and outrigger system will be designed to comprise an integrated assembly, removable from the carrier vehicle as a single self-supporting unit.  The design will facilitate repair, modifications or replacement of the aerial device, apparatus body, or chassis individually, as required by wear from use, obsolescence, or for purposes of refurbishment.

SINGLE-LINE RESPONSIBILITY

KME is providing single source manufacturing. KME designs, manufactures and builds our own fire apparatus cab, chassis and body. This capability provides a consistent design and manufacturing procedures that will reduce warranty issues and provide ease in parts replacement.

PRODUCT LIABILITY INSURANCE

KME is providing liability and facility insurance equaling $25,000,000.00, which is one of the highest available in the fire industry.  Reference attached documentation.

SERVICE CENTER AND PARTS DEPOT

Antietam Fire Apparatus, Inc.

KME FIRE APPARATUS SERVICE STATEMENT

The proposed KME Fire Apparatus vehicle is offered with service for in or out of warranty repairs can be promptly performed by the local KME authorized service center.

Service is provided by:

Antietam Fire Apparatus, Inc.

19932 Beaver Creek Rd.

Hagerstown, MD  21740

Phone:	(877) 378-2781 / (301) 797-1410

Cell:   	(301) 730-4018

Fax:    	(301) 797-1412

Service Center Capabilities

Antietam Fire Apparatus, Inc. celebrates its 18 th year of operation and employs ten (10) people and is proud to operate a Service Center in Hagerstown, MD. The privately owned operation employs four (4) full-time service mechanics to handle any service-related problems or improvements that you may desire.

Antietam Fire Apparatus, Inc. is a Hale Master Parts and Service Center that operates an on the road service truck that can offer In Station Service repairs to your apparatus if needed.

Antietam Fire Apparatus, Inc. offers twenty-four (24) hour service in which assigned service personnel carry pagers; one (1) man is always on call to handle any truck that is down and out of service.

The service facilities provide service to handle sheet metal repair and fabrication, pump and electrical repair, aerial ladder service, and effect booster tank enlarging and replacement, and minor or major refurbishment capabilities.

Service and repairs to all makes of fire apparatus including trucks with Hale, Waterous, Darley, FMC and John Bean Pumps.

The Service Center employees are fully insured with Workmans Compensation, at 3 Million Dollar Garage Keepers Liability Insurance Coverage and a 1 Million Dollar Products Liability Insurance Policy to protect your fire department in case of injury to personnel or your fire department equipment.

PRICES AND PAYMENTS

The bid price will be F.O.B. Destination, on a delivered and accepted basis at the Fire Department.

Total price on KME's proposal sheet will include all items listed in these specifications.  Listing any items contained in the specification as an extra cost item, unless specifically requested to do so in these specifications, will automatically be cause for rejection.

KME will compute pricing less federal and state taxes.  It is understood that any applicable taxes will be added to the proposed prices, unless the purchaser furnishes appropriate tax-exempt forms.

DELIVERY TIME

KME is proposing to complete the apparatus delivery time based on the number of calendar days, starting from the date the sales contract is signed and accepted by KME Fire Apparatus.

Delivery Time: 270 - 330 Calendar Days

MATERIAL AND WORKMANSHIP

All equipment furnished will be guaranteed to be new and of current manufacture, to meet all requirements of purchaser's specifications.

All workmanship will be of high quality and accomplished in a professional manner so as to insure a functional apparatus with a pleasing, aesthetic appearance.

SALES ENGINEER

KME will designate an in house individual to perform the contractor's sales engineer functions.  The sales engineer will provide a single point interface between the purchaser and KME on all matters concerning the contract.

APPROVAL DRAWING

A detailed drawing of the apparatus will be provided to the Mardela Springs Volunteer Fire Company for approval before construction begins.  A copy of this drawing shall also be provided to the manufacturer's representative. Upon Mardela Springs Volunteer Fire Company approval, the finalized drawing shall become a part of the total contract.

The drawing shall show, but is not limited to, such items as the chassis make and model, major components, location of lights, sirens, all compartment locations and dimensions, special suctions, discharges, etc.  The drawing shall be a visual interpretation of the apparatus as it is to be supplied.

INSPECTION VISITS

KME will provide three (3) factory inspection trips to KME's facility.  Transportation, meals, lodging, and other requisite expenses will be the bidder's responsibility.

Accommodations shall be for four (4) Fire Department representatives per trip.

The factory visits shall occur at the following stages of production of the apparatus:

Pre-construction / blueprint review.

Mid point completion of entire apparatus.

Final inspection upon completion.

Travel arrangements less than 300 miles from the manufacturing facility shall be via ground transportation.

The customer maintains the right to inspect the apparatus, within KME's normal business hours. At any other point during construction expenses incurred during non-specified visits shall be the responsibility of the customer.

During inspection visits, the customer reserves the right to conduct actual performance tests to evaluate completed portions of the unit.  Testing shall be accomplished with the assistance and resources of the contractor.

DELIVERY

Delivery of the apparatus to the Fire Department will remain KME's responsibility.

A qualified and responsible representative of KME will deliver the apparatus to the Fire Department.

INSTRUCTION MANUALS/DRAWINGS, SCHEMATIC

KME will supply at time of delivery, two (2) copies of a complete operation and service manual covering the complete apparatus as delivered and accepted.

The manual will contain the following:

- Descriptions, specifications, and ratings of chassis, pump (if applicable), and aerial device 
(if applicable).

- Wiring diagrams

- Lubrication charts

- Operating instructions for the chassis, any major components such as a pump and any 
auxiliary systems.

- Instructions regarding the frequency and procedures recommended for maintenance.

- Parts replacement information.

PRINCIPAL APPARATUS DIMENSIONS & G.V.W.R.

The principal dimensions of the completed apparatus will not exceed the following maximum acceptable dimensions:

KME's PROPOSED DIMENSIONS:

- OVERALL LENGTH:	449"

- OVERALL WIDTH:	100"

- OVERALL HEIGHT:	126"

- WHEELBASE:		228"

KME will include the principal dimensions, front G.A.W.R., rear G.A.W.R., and total G.V.W.R. of the proposed apparatus.  Additionally, KME will provide a weight distribution of the fully loaded, completed vehicle; this will include a filled water tank, specified hose load, miscellaneous equipment allowance in accordance with NFPA-1901 requirements, and an equivalent personnel load of 250 lbs. per seating position.

PRE-DELIVERY SERVICE

Included in the KME proposal and after transportation from the factory or immediately prior to delivery to the fire department, the apparatus will receive a pre-delivery service consisting of: engine oil & filter change, chassis lubrication, fuel filter(s) changed, adjustment of engine to manufacturers specifications, complete inspection including all electrical and mechanical devices, for proper operation and correction of leaks or obvious problems.

KME OWNERSHIP

KME is a tightly held family owned corporation. All of the stockholders are members of the Kovatch family of Nesquehoning, PA. KME carries no (zero) long term debt and is the largest privately owned manufacturer of fire apparatus in the country.

FAMA MEMBERSHIP

KME Fire Apparatus is a leading and proud member of the Fire Apparatus Manufacturer's Association (FAMA).

U.S.A. MANUFACTURER

The entire apparatus shall be assembled within the borders of the Continental United States to insure more readily available parts (without added costs and delays caused by tariffs and customs) and service.

QUALITY MANAGEMENT

KME Fire Apparatus operates a Quality Management System under the requirements of MIL-I-45208A, a military specification for a quality inspection system established to substantiate product conformance to drawings, specifications, and contract requirements.  A copy of the certificate of compliance will be included in the bid.

STEPPING, STANDING, & WALKING SURFACES

All stepping, standing, and walking surfaces on the body will meet NFPA #1901 anti-slip standards.  Aluminum tread plate utilized for stepping, standing, and walking surfaces will be Alcoa No-Slip type. This material will be certified to meet the NFPA #1901 standard.  Upon request by the purchaser, KME will supply proof of compliance with this requirement.  All vertical surfaces on the body, which incorporate aluminum tread plate material, will utilize the same material pattern to provide a consistent overall appearance.

UNDERWRITERS LABORATORIES INC. (UL) EXAMINATION AND TEST PROPOSAL

If required by the specific chapters of NFPA-1901, the proposed unit will be tested and certified for KME Fire Apparatus by Underwriters Laboratories Inc. (UL) Underwriters Laboratories Inc. (UL) is recognized worldwide as a leading third party product safety certification organization for over 100 years. UL has served on National Fire Protection Association (NFPA) technical committees for over thirty years.

INDEPENDENT TESTING ORGANIZATION QUALIFICATIONS

- UL is a nationally recognized testing laboratory recognized by OSHA.

- UL complies with the American Society for Testing and Materials (ASTM) Standard  ASTM E543 "Determining the Qualifications for Nondestructive Testing Agencies."

- UL has more than 40 years of automotive fire apparatus safety testing experience and 16 years of factory aerial device testing and Certification experience. UL has more than 100 years of experience developing and implementing product safety standards.

- UL does not represent, is not associated with, nor is in the manufacture or repair of automotive 
fire apparatus.

- All test work for fire pumps outlined in NFPA 1901, Edition will be conducted.

- UL has included a list of all factory aerial device manufacturers for whom testing is currently being conducted on a regular basis.

- UL carries ten million dollars in excess liability insurance for bodily injury and properly 
damage combined.

All work outlined in NFPA 1914, current Edition, including nondestructive testing, will be conducted at the manufacturer's facility.

PERSONNEL

The UL inspectors performing the test work on the units are certified to Level II in the required NDT methods, under the requirements outlined in ASNT document CP-189.

The actual person(s) performing the inspection will present for review proof of Level II Certification in the required NDT methods.

Prior to submittal to the automotive fire apparatus manufacturer, the final Report will be reviewed by the Supervisor of Fire Equipment Services and a Registered Professional Engineer, both of whom are directly involved with the aerial device certification program at UL.

GENERAL APPARATUS DESCRIPTION "MOBILE WATER SUPPLY"

The unit shall be designed to conform fully to the "Mobile Water Supply Fire Apparatus" requirements as stated in the NFPA 1901 Standard (2009 Revision), which shall include the following required chapters as stated in this revision:

- Chapter 1	Administration

- Chapter 2	Referenced Publications

- Chapter 3	Definitions

- Chapter 4	General Requirements

- Chapter 7	Mobile Water Supply Fire Apparatus

- Chapter 12	Chassis and Vehicle Components

- Chapter 13	Low Voltage Electrical Systems and Warning Devices

- Chapter 14	Driving and Crew Areas

- Chapter 15	Body, Compartments and Equipment Mounting

- Chapter 20	Foam Proportioning Systems

- Chapter 22	Line Voltage Electrical Systems

CAB SAFETY SIGNS

The following safety signs shall be provided in the cab:

- A label displaying the maximum number of personnel the vehicle is designed to carry shall

be visible to the driver.

- “Occupants must be seated and belted when apparatus is in motion” signs shall be visible

from each seat.

- “Do Not Move Apparatus When Light Is On” sign adjacent to the warning light indicating a

hazard if the apparatus is moved (as described in subsequent section).

- A label displaying the height, length, and GVWR of the vehicle shall be visible to driver.

- This label shall indicate that the fire department must revise the dimension if vehicle height

changes while vehicle is in service.

CHASSIS DATA LABELS

The following information shall be on labels affixed to the vehicle:

Fluid Data:

- Engine Oil

- Engine Coolant

- Chassis Transmission Fluid

- Pump Transmission Lubrication Fluid

- Pump Primer Fluid (if applicable)

- Drive Axle(s) Lubrication Fluid

- Air Conditioning Refrigerant

- Air Conditioning Lubrication Oil

- Power Steering Fluid

- Cab Tilt Mechanism Fluid

- Transfer Case Fluid

- Equipment Rack Fluid

- Air Compressor System Lubricant

- Generator System Lubricant

- Front tire cold pressure

- Rear tire cold pressure

Chassis Data:

- Chassis Manufacturer

- Production Number

- Year Built

- Month Manufactured

- Vehicle Identification Number

Manufacturers weight certification:

- Gross Vehicle (or Combination) Weight Rating (GVWR or GCWR)

- Gross Axle Weight Rating, Front

- Gross Axle Weight Rating, Rear

ROLLOVER STABILITY

The apparatus shall meet the criteria defined in 4.13.1 for rollover stability as defined in the 2009 NFPA  Standard for Automotive Fire Apparatus.

"PREDATOR XL" CAB TYPE

- FULL TILT

- CONTOUR WINDSHIELD

The cab shall be a custom tilt style, built specifically for fire service. The cab shall be a cab over engine design, with integral tilt mechanism and engine access from inside the cab.

Cab shall be designed, fabricated, assembled in its entirety, and installed on the frame rails in the factory of the bidder. This requirement shall eliminate any split responsibility in warranty and service. NO EXCEPTIONS TO THIS REQUIREMENT.

OPEN SPACE DESIGN

The cab interior shall be the "Open-Space" design with no wall, support posts or window between the front and rear crew area to allow direct communication, better visibility and air circulation in the cab.

CAB MATERIAL

The cab shall be fabricated from 5052-H 32 aluminum alloy, utilizing the minimum material thickness as follows:

- Cab side panels	0.125 thick (1/8")

- Cab roof	0.125 thick (1/8")

- Forward cab front sheet	0.125 thick (1/8")

- Interior cab panels	0.125 thick (1/8")

- Other panels	0.125 thick (1/8")

- Cab doors	0.1875 thick (3/16")

- Engine enclosure side panels	0.250 thick (1/4")

CAB - BASE CONSTRUCTION

Cab sub-frame shall be a welded assembly fabricated of 6063 structural aluminum alloy. This frame shall extend the full length and width of the cab and be secured to the chassis frame through two (2) rear urethane self centering load cushions, two (2) forward pivot brackets, and two (2) cab locks.  The cab shall be of entirely welded construction.

The front cab wall shall be of double wall type construction, featuring an inner and outer panel.  (No Exceptions)

CRASH TESTING CERTIFICATION

To ensure the safety of the cab occupants and cab integrity, proof of third party testing shall be provided.  The cab shall be certified for SAEJ2422 side impact, SAEJ2420 with ECER29 cab front impact, and ECER29 cab roof strength. NO EXCEPTIONS

DIMENSIONS - LONG FOUR DOOR STYLE CAB

Minimum Cab Dimensions:

- Overall width		96"

- Inside width across ceiling		88"

- Front area floor to ceiling		63"

- Top of front seat to ceiling		44" (depending upon seat type)

- Seat back to steering wheel		22" (depending upon seat type)

- Inside width (door to engine enclosure)		25" (driver's side, at floor)

- Inside width (door to engine enclosure)		22-1/2" (officer's side, at floor)

- Crew seat area width		88"

- Outer crew seat risers to rear wall		49-1/2"

- Centerline axle to rear wall		67-1/2"

- Rear of engine enclosure to rear cab wall	50"

- Centerline axle to front of cab		74"

- Floor to top of engine enclosure		31-1/2"

Glass Area Dimensions:

- Windshield (Contour)		2,900 sq. in.

- Front door window, retractable		743 sq. in. each

- Rear door window, retractable		875 sq. in. each

- Side fixed crew windows		620 sq. in. each

CAB ROOF

The roof shall be of a split level design with radius edges for an aesthetic, streamline appearance.  The roof shall be constructed the same material as the main structure and shall be internally reinforced using framing which shall span the entire width and length of the cab for maximum structural integrity. This shall allow the roof to support personnel and roof mounted equipment without the need for additional reinforcement.

The cab roof over the rear crew area shall be raised twenty two (22) inches higher than the front driver and officer area.  The front face of the raised roof section shall be sloped at a 45 degree angle, creating a streamlined interface with the standard, lower, forward roof section.  This design shall allow for additional interior height in the rear crew area.

The rear crew area doors shall be "Vista-Style", extending full height to the radius edge of the raised roof.

Approximate dimensions:

- Crew area floor to ceiling	75-1/2"

- Top of crew seat to ceiling	57" (depending upon seat type)

CAB ROOF DRIP RAIL

For enhanced protection from inclement weather, a drip rail shall be furnished on the sides of the cab.  The drip rail shall be constructed of bright polished extruded aluminum, and be fastened to the sides of the cab rood edge.  The drip rail shall extend the full length of the cab roof.

CAB DOORS

Four (4) side-opening doors shall be provided.  The cab doors shall be totally aluminum construction with an extruded aluminum frame and a 3/16" thick aluminum outer door skin.  Doors shall be full height from the step to the cab roof rain gutter and enclose the step area when the doors are closed.

The forward cab door opening shall be a minimum of 37" wide, and the rear cab door opening shall be a minimum of 31" wide.  The rearward cab doors shall have a radius cutout allowing the door opening to protrude forward over the cab wheel well, while providing full access to the rear crew area.

There shall be a heavy duty piano type stainless steel hinge on each door with a minimum pin diameter of 5/16". Hinges shall be slotted for ease of horizontal and vertical adjustment.  There shall be a cab door seal and the doors shall close flush with the side of the cab.  A heavy-duty 6" wide belting material shall be utilized to prevent the cab doors from opening greater than 90 degrees.

ENTRY STEP AREA

Each of the forward entrance steps shall be a minimum of 8-1/2" deep x 30" wide with the floor board recessed a minimum of 3" to avoid "shin knocking".  Each step shall be fabricated as an integral part of the cab construction. The cab step and risers shall be overlaid with bright finish aluminum tread plate.

Each of the rear entrance steps shall be a minimum of 8-1/2" deep x 20" wide.  An intermediate step shall be provided between the lower entrance step and the crew area floor for ease of entry and egress.  Each set of steps and respective step risers shall be constructed as an integral part of the cab construction and shall be overlaid with bright finish aluminum tread plate.

Cab Entry Door Dimensions:

- Forward door opening	73" high x 37" wide

- Forward door recessed step	30" wide by 8-1/2" deep

- Rear door opening	95-3/4" high x 31" wide

- Rear door recessed step	20" wide x 8-1/2" deep

DOOR LATCHES

Heavy-duty, bright finish cast paddle latches shall be provided on the interior and exterior of each cab door. Door latch mechanisms which utilize spring steel clamps shall not be considered due to their tendency to both rust and break.  The interior door latch cables are to be designed to reduce adjustment or possible wear at the adjustment turnbuckles.

Each exterior cab door latch shall be equipped with keyed locks.  The cab doors shall only be capable of being locked from the exterior of the cab.

Each exterior cab door shall be equipped with keyed locks.  The cab doors shall be capable of being locked from the outside with a key and from the inside with a push-pull control installed in each door.

DOOR WINDOWS

Each side cab door shall have a tinted retractable window operated by a hand crank mechanism. The window track shall be designed into the door frame extrusion, which shall be extruded with a track groove to house a window track and seal. The window shall be capable of being removed from an access slot designed in the bottom of the door frame.

Each side cab door window shall be designed with a custom extruded trim plate, which shall conform to the perimeter of the window cut out in each door. The trim plate shall extend from the edge of the door skin to the window and shall have a silver anodized finish.

INNER DOOR PANELS

The upper section of each cab door interior shall have a formed ABS door panel, which shall be vacuum overlaid with a soft vinyl upholstery material.  The color of the panel upholstery shall be gray. The ABS door panels shall terminate approximately ten (10) inches above the cab floor.

The lower and full width portion of each door interior shall have brushed stainless steel scuff plates to provide maximum wear protection.  These plates shall extend  above the inside cab floor level when the doors are closed.

DOOR WARNING - CHEVRON

Four (4) Chevron reflective signs shall be installed on the lowest portion of the inner door panels, one (1) on each door.  These chevrons shall cover at least 96 in².

CAB DOOR FRAME AND JAMB SCUFF PLATES

A polished stainless steel trim plate shall be provided rearward of each cab door opening to protect the vertical cab corner rearward of the door opening and on the cab door striker posts to protect the cab paint when exiting and entering the cab.

CAB TRIM

The cab shall have accent molding on the front and sides of the cab below the windows and windshield.

EXTERIOR CAB WALL OVERLAY

A bright finish aluminum tread plate overlay shall be provided on the exterior rear cab wall.  The tread plate overlay shall be sealed with caulking around the edges to prevent moisture from getting between the cab and the overlay.

EXTERIOR CAB COMPARTMENTS

Two (2) compartments shall be provided, to the rear of the crew cab doors.  These compartments shall be approximately 18" high, 10" wide and 25 3/4" deep.  Compartment door shall have a 3/16" aluminum exterior skin door with a one (1) inch box pan and a stainless steel "D" ring handle. Door shall be hinged on the forward edge with a stainless steel vertical piano hinge so it opens toward the rear cab door.  The door shall be held in the open position by a gas shock stay arm.

Each compartment shall contain a flush mounted light for illumination of the compartment and shall be wired to a door jamb switch to automatically come on when the door is opened.

WINDSHIELD/GLASS

A one piece, symmetrical, safety glass windshield shall be provided on the cab for the driver and officer providing a clear viewing area.  The windshields shall be full width to the center of the front cab support for each side and provide the occupants with a panoramic view.  To provide enhanced peripheral vision on each side of the cab, the windshield and cab structure shall be designed with radius corners, which provide a minimum of  8" of glass area, measured from the glass face to the side edge near the door post. The windshield shall consist of three (3) layers; the outer light, the middle safety laminate and the inner light.  The thick outer light layer shall provide superior chip resistance, the middle safety laminate layer shall prevent the windshield glass pieces from detaching in the event of breakage and the inner light shall provide yet another chip resistant layer.

The windshield will be a contour design with 2900 sq. in. of area for improved visibility and style. The windshield glass shall be designed so it can be used on either the driver or officer side. Windshields that are epoxied or bonded to the cab structure will not be acceptable.

WINDSHIELD WIPERS AND WASHER

Dual, electric operated, pantographic type windshield wipers shall be provided. One (1 ) electric drive motor shall be provided for each wiper.  Windshield wiper systems which utilize a single motor and a reciprocating actuator arm shall not be considered.

Wipers shall have "HI/LO" and "INTERMITTENT" operating speeds.  "HI/LO" speeds shall be controlled by a dash mounted rocker switch.  "INTERMITTENT" operation shall be controlled by a dash mounted "paddle/lever" switch.  The wipers shall be of the self-parking type.

Windshield washers shall be electric operated wet-arm type with a 3/4 gallon washer fluid reservoir, mounted inside the engine enclosure and readily accessible through the engine hatch at the rear of the engine enclosure. The washer control shall be integral with the intermittent wiper control switch.

There shall be individual removable panels on the front face of the cab for access to the wiper motor assemblies.

CAB SIDE VIEWING WINDOWS

A fixed, tinted window with 620 sq. in of glass area shall be provided on each side of the cab behind the forward cab doors. This window shall be the same height as the window in the rear cab door for maximum visibility.

DARK TINTED REAR WINDOW GLASS

The windshield and the forward cab door glass shall be provided with standard DOT green automotive tint. The side cab windows to the rear of the front doors, the rear cab door windows and any rear viewing windows shall be equipped with a dark automotive tint.  The use of stick on material shall not be acceptable.

GRAB HANDLES

Four (4) 1-1/4" diameter x 28" long, knurled, bright anodized aluminum handrails shall be provided, one (1) at each cab door entrance.  Grab rail stanchions shall be chrome plated and offset when necessary to prevent "hand-pinching" when opening or closing the doors.  Formed rubber gaskets shall be provided between each stanchion base and the cab surface.

INTERIOR GRAB RAILS

Four (4) vertically mounted 12” black cast aluminum “D” style entry assist handles shall be installed, one (1) on each side of the cab interior on the “A” post and one (1) on each side of the cab interior on the “C” post in the crew area to assist in entry and exiting of the cab.

Each front cab door shall be provided with one (1) horizontally mounted, 11" long, black cast aluminum "D" style entry assist handle on the interior door panel to assist in entry and exiting of the cab and for closing the door.

Each rear cab door shall be provided with one (1) horizontally mounted, 11" long, black cast aluminum "D" style entry assist handle on the interior door panel to assist in entry and exiting of the cab and for closing the door.  Each rear cab door shall also be provided with one (1) horizontally mounted, 30"  long black cast aluminum "D" style assist handle, located approximately 8" above the bottom of the window opening.

AIR INTAKE/OUTLET

There shall be a front air intake with a minimum of  945 square inches of open area for maximum air flow to the charge air cooler and the radiator.

Two (2) air inlets/outlets with a minimum of 43.5 square inches per inlet shall be provided horizontally above the wheel well opening, one on each side of the cab.  The design shall permit proper ducting of air through the engine compartment and cooling system. The left side inlet, used for the air intake to the air cleaner, shall be equipped with an ember separator for separating water and burning embers from the air intake system. This system shall be such that particles larger than .039 inches (1 mm) in diameter can not reach the air filter element.

The air intake and outlets shall be covered with polished stainless steel louvers, secured with polished cast aluminum housings.

WHEEL WELL LINERS

The front cab wheel wells shall be equipped with fully removable, bolt-in, aluminum inner wheel well liners.  The liners shall extend full depth into the truck frame.  The completely washable wheel well liners shall be designed to protect the cab substructure, inner panels, and other miscellaneous installed components from road salts, debris, dirt accumulation and corrosion. Fender liners which are fixed partially removable or one piece liner/fenderette shall not be considered.

FENDERETTES

The cab wheel well openings shall be trimmed with replaceable, bolt-in, polished stainless steel fenderettes.  The fenderettes shall be secured to the cab with stainless steel threaded fasteners along the internal perimeter of the wheel well.  Rubber welting shall be installed between the fenderettes and the cab side panel.

MUD FLAPS, FRONT

Heavy duty, black rubber type mud flaps shall be provided behind the front wheels.

CAB MIRRORS

Each forward cab door shall have a 16" x 6-1/2", heated and motorized, stainless steel, West Coast type mirror mounted on a swing-away, bow type, stainless steel bracket. Each mirror shall be individually remote controlled from the driver's position. The mirror heating elements shall be controlled by a single dash mounted switch. Two (2) 6" diameter, stainless steel, convex spot mirrors shall also be provided, one (1) on each main mirror bracket.

INTERIOR CAB TRIM

The cab interior shall be constructed to create an ergonomically designed interior to be user friendly and functional for the driver and officer.

The forward overhead panel shall be covered with a one-piece custom formed ABS vinyl overlay, which shall have integrated windshield defroster/heat vents.

All ABS formed material panels, as well as all of the interior upholstery panels shall be gray in color.  The upholstered cab overhead and side wall portions shall utilize gray Durawear upholstery with padding underneath to provide additional insulation.

The interior metal surfaces of the cab shall be finish painted with a textured gray paint.

INTERIOR REAR WALL

The interior rear wall of the cab shall be covered with padded gray Durawear upholstery to give durability and to match the other upholstered areas of the cab.

A twelve (12) inch high bright finish aluminum tread plate scuff plate shall be provided on the lower portion of the rear interior cab wall.

STORAGE COMPARTMENTS

There shall be a compartment provided under each front seat with a latched access door.  The compartment shall measure 8-3/4"W x 7-7/8"D x 4-3/4"H.

PREMIUM SOUNDPROOFING FLOORING

The floor of the driver compartment and crew area shall be lined with premium sound proofing material.  Additionally, the cab overhead and rear wall shall be insulated with a foam insulation, located between the cab upholstery and cab outer skin.

ENGINE ENCLOSURE

The forward portion of the engine enclosure shall be covered with a vinyl ABS material formed overlay to match the balance of the cab interior.  To allow maximum "elbow room"  for the driver and officer, the forward portion of the engine enclosure shall feature a contour shape.  The engine enclosure shall not significantly obstruct the driver's vision in any direction.  The enclosure shall be an integral part of the cab structure, which shall be constructed from .250 5052-H32 aluminum, providing adequate strength to support radio, map boxes, etc.  The engine enclosure shall be insulated to protect  from heat and sound.  The noise insulation shall keep the DBA level within the limits stated in the current NFPA series 1900 pamphlet.

ENGINE COMPARTMENT ACCESS DOOR

A padded, hinged access door shall be provided in the top rearward portion of the engine enclosure.  The door shall allow access to the engine oil, transmission fluid, power steering fluid level dipsticks and the windshield washer fluid reservoir.  The access door shall be provided with two (2) flush mounted latches and gas shock holders.  There shall be a vinyl ABS material cover over the access door to give a cleaner look to the top of the engine enclosure and doghouse area.

DRIVER'S SEAT

The driver's seat shall be a H. O. Bostrom Sierra Air-50FX/HD air suspension, high back bucket seat. The seat shall have a tapered and padded seat cushion with lumbar support. The seat shall have a five inch fore and aft adjustment, a three inch height adjustment with heavy duty damper and a fixed seat back. The seat air ride suspension shall be pneumatically controlled from a control switch on the forward lower edge of the seat.

A red 3-point shoulder harness with lap belt shall be provided as standard equipment.

OFFICER'S SEAT

The officer's seat shall be a H. O. Bostrom Tanker 450 Air-50 series air-suspension, high back bucket seat.  The seat shall have a tapered and padded seat cushion with lumbar support.  The seat shall have a five inch fore and aft adjustment, a three inch height adjustment with heavy duty damper and a reclining seat back.  The seat shall include a SCBA storage area with integral headrest.  The seat air ride suspension shall be pneumatically controlled from a control switch on the forward lower edge of the seat.

A red 3-point shoulder harness with lap belt shall be provided as standard equipment.

The officer's seat shall include a H. O. BOSTROM Secure All™ SCBA Locking System.  The bracket system shall be free of straps and clamps that may interfere with auxiliary equipment on SCBA units. The center guide fork shall keep the tank in-place for a safe and comfortable fit in seat cavity. Fire fighters shall simply push the SCBA unit against the pivot arm to engage the patented auto-locking system. Once the lock is engaged, the top clamp shall surround the top of the SCBA tank for a secure fit in all directions.

The standard release handle shall be integrated into the seat cushion for quick and easy release and shall eliminate the need for straps or pull cords to interfere with other SCBA equipment.

CREW AREA SEATING, LFD CAB

DRIVER'S SIDE REAR FACING CREW SEAT

The driver's side outboard rear facing crew seat shall be a H. O. Bostrom Tanker 450 ABTS series fixed base high back bucket seat.  The seat shall have a tapered and padded seat cushion with lumbar support.  The seat shall include a SCBA storage area with integral headrest.

The seat shall be equipped with a red integrated 3-point shoulder harness with lap belt and an automatic retractor built into the seat assembly.

The driver's side rear facing outboard seat shall include a H. O. BOSTROM Secure All™ SCBA Locking System.  The bracket system shall be free of straps and clamps that may interfere with auxiliary equipment on SCBA units. The center guide fork shall keep the tank in-place for a safe and comfortable fit in seat cavity. Fire fighters shall simply push the SCBA unit against the pivot arm to engage the patented auto-locking system. Once the lock is engaged, the top clamp shall surround the top of the SCBA tank for a secure fit in all directions.

The standard release handle shall be integrated into the seat cushion for quick and easy release and shall eliminate the need for straps or pull cords to interfere with other SCBA equipment.

OFFICER'S SIDE REAR FACING CREW SEAT

The officer's side outboard rear facing crew seat shall be a H. O. Bostrom Tanker 450 ABTS series fixed base high back bucket seat.  The seat shall have a tapered and padded seat cushion with lumbar support.  The seat shall include a SCBA storage area with integral headrest.

The seat shall be equipped with a red integrated 3-point shoulder harness with lap belt and an automatic retractor built into the seat assembly.

The officer's side rear facing outboard seat shall include a H. O. BOSTROM Secure All™ SCBA Locking System.  The bracket system shall be free of straps and clamps that may interfere with auxiliary equipment on SCBA units. The center guide fork shall keep the tank in-place for a safe and comfortable fit in seat cavity. Fire fighters shall simply push the SCBA unit against the pivot arm to engage the patented auto-locking system. Once the lock is engaged, the top clamp shall surround the top of the SCBA tank for a secure fit in all directions.

The standard release handle shall be integrated into the seat cushion for quick and easy release and shall eliminate the need for straps or pull cords to interfere with other SCBA equipment.

CENTER FORWARD FACING CREW SEATS

Two (2) center inboard forward facing crew seats shall be provided, each seat shall be an H. O. Bostrom Tanker 450 ABTS series fixed high back bucket seat.  Each seat shall have a tapered and padded seat cushion with lumbar support.  Each seat shall include an SCBA storage area with integral headrest.

Each seat shall be equipped with a red integrated 3-point shoulder harness with lap belt and an automatic retractor built into the seat assembly.

The two (2) center inboard forward facing crew seats shall have a flip-up style seat bases.

The center forward facing seats shall include a H. O. BOSTROM Secure All™ SCBA Locking System.  The bracket system shall be free of straps and clamps that may interfere with auxiliary equipment on SCBA units. The center guide fork shall keep the tank in-place for a safe and comfortable fit in seat cavity. Fire fighters shall simply push the SCBA unit against the pivot arm to engage the patented auto-locking system. Once the lock is engaged, the top clamp shall surround the top of the SCBA tank for a secure fit in all directions.

The standard release handle shall be integrated into the seat cushion for quick and easy release and shall eliminate the need for straps or pull cords to interfere with other SCBA equipment.

SEAT UPHOLSTERY MATERIAL

The seats shall be upholstered with heavy duty black Durawear material as provided by Bostrom.

SEAT BELT CUSHION SENSORS AND BELT SENSORS

The apparatus shall be equipped with a IMMI seat belt warning system. The system shall consist of a Seat Belt module, dash mounted display and an audible alarm.

Seat belt and seat cushion sensors shall be provided on the six (6) specified seating positions.

CAB HELMET STORAGE

Each seat position shall have a ZICO:  Ziamatic UHH-1 Crew Cab Helmet Holder, meeting NFPA 1901, 2009 for a total of six (6) holders.

VEHICLE DATA RECORDER

An IMMI Vehicle Data Recorder (VDR) system shall be provided. The system shall include an NFPA compliant "Black Box" with reporting software that shall be capable of data storage to coincide with the NFPA requirements.

Data storage capabilities shall include interfaces with the following systems:

- Display module (Master Optical Warning Device)

- Seat belt monitoring (seat occupied with seat belt)

- Surface or panel mount

- VDR, date & time stamp

- Max Vehicle speed (MPH)

- Vehicle acceleration / deceleration (MPH/Sec.)

- Engine Speed (RPM)

- ABS event

- Data password protected

- Data sampled once per second, in 48-hour loop

- Data sampled min by min for 100 engine hours

- Throttle position (% of Throttle)

- Data software

- Data interface for data download

- PC / Mac Compatible

- Hours Driven

- Data summary reports

- Last Minute Log

- Idle Time

- Track inputs from RollTek (If Equipped)

SUN VISORS

To provide maximum protection for the driver and officer, two (2) padded sun visors measuring 19"L x 7-1/2"W, with shock retainers, shall be recess mounted in the cab overhead on each side.

INTERIOR CAB STORAGE COMPARTMENT

A  dual storage compartment shall be mounted in the cab in lieu of the forward facing outboard driver’s side and officer’s side crew seats.  Each compartment shall be approximately 46" high x 21" wide X 14" deep.  Each door opening shall be approximately 41 7/8" high x 18" wide.

The compartments shall be constructed of aluminum, painted with textured paint matching the interior color of the cab and shall be equipped with roll-up doors.

ADJUSTABLE SHELF OR SHELVES

Four (4) adjustable shelf(s) shall be provided in the EMS compartment.  The shelf(s) shall be constructed from 3/16" brush aluminum mounted to uni-strut tracking material.

CAB COMPARTMENT LIGHTS

The EMS compartment shall be equipped with one (1) ROM V2 brand LED interior track light(s).  The lighting shall be wired to automatically activate when the compartment door is open and the master battery switch is in the "on" position.

DASH & CENTER CONSOLE

The dash shall be constructed of vinyl overlaid, custom formed aluminum, creating an ergonomically designed interior that will be user friendly and functional for the driver and officer. The instrument cluster shall be centered in front of the driver and all gauges shall be installed in the non-glare, pewter finish  instrument panel.

All warning lights and indicators shall be located in either the gauge itself or in the warning light cluster located in the lower center portion of the dash. Each gauge shall be equipped with an international  symbol that is easily recognizable, denoting the system being monitored. Instrumentation shall be backlit for easy identification.

The transmission gear selector and the spring brake control valve shall be located on the left side of the center dash assembly, toward the driver for easy access.

There shall be provisions for mounting of switch panels in the center of the dash between the driver and officer.  The top center of the dash assembly shall contain one (1) large removable access door for access to the main chassis wiring panels and breaker panels.

DRIVERS DASHBOARD PANEL

The main instrument panel shall be centered in front of the driver and shall be hinged at the bottom with two ¼ turn latches at the top.  The driver dash panel shall be 1/8” aluminum with an anti-glare, pewter brushed surface.  The drivers dashboard panel shall contain the gauge panel and a two level instrument warning light cluster.

The lower portion of this panel can be used for the installation of up to five (5) guarded type rocker switches. Examples of the switches that shall be installed in this area are automatic chains, fan clutch over-ride, ATC mud-snow, inter-axle diff lock, electric fuel pump, all wheel drive, etc.

An ignition and engine start switch shall be located on a panel to the left upper portion of the driver's side dash panel.

The main instrument panel shall contain ten (10) primary gauges. Each gauge shall have a raised glass lens with black matte finish trim ring and be backlit by integral white LED's.  Each gauge shall be designed with an integral red warning light with a pre-programmed warning point.  Gauges monitoring drive-train component status shall be of the direct data bus type capable of displaying information broadcast on the J 1939 data-link.  Each gauge warning indicator shall be capable of activating an audible alarm inside the dashboard.

The ten (10) primary gauges shall consist of:

- Vehicle speedometer (0-80 mph) with digital odometer

- Engine tachometer (0-3000 rpm) with digital hour meter

- Engine oil pressure (0-100 psi); low oil pressure warning

- Engine coolant temperature (100-280 °F);  high engine temp warning

- Transmission oil temperature (100-350 °F); high transmission fluid temp warning

- Vehicle battery voltage (9-18 VDC); low voltage warning

- Front air system gauge (0-150 psi); low air pressure warning at 65 psi

- Rear air system gauge (0-150 psi); low air pressure warning at 65 psi

- Fuel level  (E-1/2-F); low fuel level  warning

- Air cleaner restriction gauge (0-40), warning at 25" Inter axle lock control switch

- Secondary fuel primer control switch

- Engine Compression Brake Controls

Additional auxiliary control switches and instruments (if applicable) shall be located within the dash panel and overhead panel located near the driver's position.

DIGITAL CLOCK

Odyssey, dash mounted digital clock will be installed at location determined at pre-construction.

INDICATOR CLUSTER

The driver's dashboard panel shall contain an Ametek instrument warning light cluster and gauges.

The display contains the system control unit that collects data from the vehicle data bus (J 1939), analog sensors, and switches throughout the vehicle.  This data shall be presented using gauges, telltales and the display.  The display shall include 18 telltales and 2 buttons to navigate through the screen menus.

The LCD module shall be a 2 line by 20-character display with each character being 7 by 5 dot matrix configuration.  FSTN technology shall be used on the display for wide viewing capability.  The module shall be backlit with amber LED's.  The unit shall also be supplied with a heater to ensure proper operation in inclement weather.

The display contains a series of screens to provide information about the vehicle and to control the display of that information. The screens are divided into menus that can be displayed while the vehicle is in motion and menus that can only be accessed when the park brake is set.

On the Road displays include:

- Two (2) user configurable displays that can display any of the parameters the display collects. This includes odometer, trip information, fuel economy information; all gauge data, and virtually any other data available on the vehicle.

- Two (2) trip displays for miles and hours that are capable of being reset.

- Two (2) fuel data screens: one for fuel remaining until empty and one for fuel economy. The fuel economy display is capable of being reset so that average economy over an operator determined period can be displayed.

The additional displays that can be accessed when the park brake is set are as follows:

- Engine hours as maintained by the engine ECU

- Service Alarm screens that report miles to next service or miles service is overdue. These screens also allow the operator to choose the length of the service alarm and to reset it.

- Message screens provide access to the warning messages the display has collected during the current ignition cycle.  These screens are divided into the configured warnings like “Low Air Pressure” and the data bus faults reported by ECU's on the vehicle. Both lists allow the operator to review the last 12 events that occurred on the vehicle for maintenance and troubleshooting purposes.

- Diagnostic screens provide a means to test the instrumentation system to verify it is working correctly.

- Setup screens provide a way to set the message center for display English or metric. They also allow the operator to choose the data that shall be displayed in the configurable on-the-road screens.

The system can be configured with user defined warning messages as shown below. When these events occur the warning message shall come up on the screen and can be accompanied by a buzzer. The messages can be prioritized so the most important messages are always displayed and messages that have been dismissed but are still active are kept in the message screens for review until the ignition is turned off.  Listed below are the defined telltales and their indicators.

- "Right And Left Directional" arrows 	(green in color)

- "Ignition ON" Indicator 	(amber in color)

- "Hi Beam" indicator 	(blue in color)

- "Battery ON" indicator 	(green in color)

- "Parking Brake ON" indicator 	(red in color)

- "Check Transmission" indicator 	(amber in color)

- "Cab Not Latched" indicator 	(red in color)

- "Stop Engine" indicator 	(red in color)

- "Check Engine" indicator 	(amber in color)

- "ABS Warning" indicator 	(red in color)

- "Low Coolant Level" 	(red in color)

- "Fuel Restriction" indicator 	(amber in color)

- "Water In Fuel" indicator 	(amber in color)

- "Fasten Seat Belts" indicator 	(red in color)

- "Fast Idle" Indicator 	(amber in color)

- "Do Not Move Truck" indicator 	(red in color)

- "DPF Regeneration"	(amber in color)

- "Exhaust High Temperature"	(amber in color)

- "Engine Diagnostic Fault"	(amber in color)

- "Retarder On"	(green in color)

- "Inter Axle Lock" indicator

- "Low Engine Coolant" indicator light and alarm

LOWER RIGHT AUXILIARY SWITCH PANEL

The driver’s lower right panel shall be capable of housing five (5) switches.  Examples of the switches that shall be installed in this area are automatic chains, fan clutch over-ride, ATC, inter-axle diff lock, electric fuel pump, all wheel drive, etc.

MOBILE TERMINAL AREA

There shall be a flat surface area in front of the officer for placement of a laptop computer.

CENTER OVERHEAD PANEL

An overhead console with a removable pewter panel shall be provided on the cab roof between the driver and officer to permit installation of cab stereo, intercom systems, arrow stick controls, etc.  The overhead console shall be approximately 27" wide x 4" high x 13" deep and shall be painted to match the interior of the cab.  The overhead console shall not obstruct the driver's vision through the officer's side window.

CLIMATE CONTROL SYSTEM

A climate-control system shall be provided for total cab environmental comfort.  This system shall provide heat, cooling and defrost capabilities to various areas in the cab. The system shall consist of two (2) evaporator units, mounted in the center overhead of the cab.  One (1) unit shall provide defrost, air conditioning and heat for the front of the cab and shall provide heating and cooling for drivers and officers feet.  One (1) unit shall provide heat and air conditioning for the back of the cab.

The ceiling mounted evaporator/heater unit for the front shall include the following:

- Dual high output blower.

- High efficiency coil that includes "rifled" tubing and oversized header tubes for maximum refrigerant distribution.

- Four (4) 3" diameter, adjustable louvers; two (2) each side of the cab overhead, facing the driver and officer seat positions.

- Four (4) 3" diameter, adjustable defroster louvers positioned above the windshield to provide optimum coverage.

- Four (4) 3" diameter adjustable louvers,  one (1) below the driver and officer seat positions and one (1) under each outboard rear facing crew seat.

- Damper controls shall be pneumatically operated to provide air discharge to the windshield, front overhead air discharge louvers or floor position as required and shall be located above the driver seat position.

- An electric water valve to control the amount of heat.

- Fully insulated housing.

- BTU:  34,000 A/C

- BTU:  50,000 Heat

- CFM: 410 @ 13.8 volts

The ceiling mounted evaporator/heater unit for the crew area shall include the following:

- Dual high output blower

- High efficiency coil which includes, "rifled" tubing and oversized header tubes for maximum refrigerant distribution

- Eight (8) 3" diameter, adjustable louvers positioned to provide optimum coverage.

- Fully insulated housing.

- BTU:  36,400 A/C

- BTU:  52,000 Heat

- CFM: 440 @ 13.8 volts

ROOF MOUNT CONDENSER

A 12-volt roof top condenser shall be strategically positioned on the cab roof so as not to interfere with any emergency lighting systems and shall include the following:

- High performance, long life fan assemblies.  Fan motors are sealed around housing and shaft areas.

- Condenser and coil design includes rifled tubing for maximum efficiency.  Coil is painted black.

- Condenser unit includes receiver drier with hi/lo pressure switch.

- Wire harness includes necessary wiring for clutch circuit as well as a separate power relay circuit.

- 14 gauge mounting brackets

- 16-gauge condenser frame and fan shroud

- 16 gauge aluminum cover, E-coated white

Mounting design will enable easy servicing of all components and unit replacement if necessary.

The ceiling mounted evaporator unit shall be covered with an ergonomically designed custom ABS panel to provide maximum headroom and a pleasing appearance.

The roof mounted air conditioning condenser housing(s) shall be painted to match the cab roof color.

CLIMATE CONTROL SWITCHES

The drivers overhead panel shall contain all controls for the cab climate control system.  The following controls shall be provided:  mode selector switch, front fan speed switch, rear fan speed switch, air conditioning on/off switch, and temperature control dial.  All controls shall be clearly labeled, adequately backlit, and installed in an easily removable panel.

CAB TILT ASSEMBLY

The cab tilt mechanism shall be custom designed for ease of maintenance and shall consist of two (2) hydraulic cylinders with a maximum lift capacity of 19,625 pounds.  Hydraulic lines shall be rated at 20,000 PSI burst pressure.  Each cylinder shall have an attached hydraulic locking mechanism, in the event of a hydraulic failure.  Hydraulic cylinders shall be detachable to allow removal of the engine for major service.  A mechanical cylinder stay bar and release shall be provided to insure a positive lock in the tilted position.

The two (2) rear outboard cab latches shall be of the hydraulic pressure release, automatic re-latching type, and provide an automatic positive lock when the cab is lowered.  The latch must not disengage or experience any damage when subjected to a pull apart tensile load of 6,000 lbs.  The hydraulic pressure required to unlock the latch shall not exceed 550 PSI.  The latch shall withstand 5,000 PSI without leaks or damage and withstand 1,000 continuous cycles of operation under a load of 1,000 lbs at liftoff.  The tilt pump shall be electric over hydraulic type, with a pressure rating of not less than 4,000 PSI.  Additionally, the cab tilt device shall be both electrically and hydraulically interlocked to prevent inadvertent activation of the cab tilt system.

- A "CAB NOT LATCHED" indicator shall be provided in the cab dash-warning cluster.

- A dual switch control system shall be provided for the cab tilt, located on the passenger side pump panel. System shall consist of a three (3) position toggle switch along with a rubber covered push button switch.

TETHER CONTROL FOR CAB TILT

A 12' tether control shall be provided to control the cab movement. This arrangement will provide the operator with a full view of the cab. The control shall include a two (2) switch control, one (1) three (3) position toggle switch and one (1) push button type switch. Both controls must be depressed for activation of the system.  The tether control shall be equipped with a detachable cord which can be plugged into a receptacle located on the front bumper.

The cab tilt control shall be equipped with an interlock that shall disable the cab tilt system , in the event the parking brake is not applied.

CHASSIS FRAME ASSEMBLY

The chassis frame shall be fabricated in its entirety in the factory of the apparatus manufacturer.  This shall prevent any split responsibility in warranty or service.

The frame shall consist of two (2) channels fastened together by cross members.  All structural fasteners used in the frame shall be Grade 8 hardware.  Hardened steel washers shall be used under all bolt heads and nuts to avoid stress concentrations.  Top flange shall be free of bolt heads.  All spring hangers shall be machined steel castings.  Weldment type chassis and the use of Huck bolts shall not be acceptable.

Each main frame rail shall be 10-1/4" x 4" x 3/8", fabricated from 110,000 PSI minimum yield steel, with a minimum section modulus of 17.97 in 4 and a resisting bending moment (RBM) of 1,976,700 inch pounds.

A full length inner frame liner shall be installed.  Total section modulus of each rail, with liner, shall be 31.20 in 4 and the total resisting bending moment (RBM) shall be 3,432,000 in-lbs, per rail.

Formed frame rails or a fish plated frame shall not be acceptable.

The chassis frame assembly, consisting of frame rails, cross members, axles and steering gear(s), shall be finish painted before installation of any electrical wiring, fuel system components, or air system components. All components or brackets fastened to the frame rails shall be cleaned, primed and painted prior to being attached to the frame rails.

FRONT BUMPER

A 10" high by full width, two (2) ribbed, bright finish, stainless steel front bumper shall be provided.  The bumper shall be wrap design to match the contour of the front cab sheet.

The bumper shall be extended 27" with a polished aluminum tread plate gravel shield enclosing the top and ends.

STORAGE WELL - DRIVER SIDE

One (1) storage well constructed of 1/8" aluminum shall be installed in the gravel shield. This storage well shall be located on the driver side of the bumper extension. The bottom of the storage well shall have a minimum of four (4) drain holes.

One (1) hinged, latched, aluminum tread plate cover shall be installed on the storage well located in the driver side of the bumper extension.

STORAGE WELL - OFFICER SIDE

One (1) storage well constructed of 1/8" aluminum shall be installed in the gravel shield. This storage well shall be located on the officer side of the bumper extension. The bottom of the storage well shall have a minimum of four (4) drain holes.

One (1) hinged, latched, aluminum tread plate cover shall be installed on the storage well located in the officer side of the bumper extension.

FRONT TOW HOOKS

Two (2) chrome plated tow hooks shall be provided, mounted below the front bumper attached directly to the frame. The tow eyes shall be fastened with grade 8 bolts and nuts.

FRONT AXLE

Front axle shall be a Meritor MFS-20-133 A-N, includes low friction "Easy Steer" bushing technology for maximum steering ease and longer life.

The front axle shall be rated at 22,500 lbs. (Minimum)

FRONT DISC BRAKES

Meritor EX-225 H, 17" disc brakes shall be provided for the front axle.  The front brakes will  be full air actuated with automatic slack adjustment.

FRONT AXLE OIL SEALS

Premium oil seals with viewer glass shall be provided on the front axle.

FRONT SUSPENSION

Front suspension shall be progressive rate front leaf springs.  The spring shall be permanently pinned at the front and have a shackle double pinned mounting at the rear.  Suspensions allowing the spring to float freely at the ends without a permanent pin shall not be acceptable.

The front leaf springs shall have a minimum of 10 leaves, a minimum length of 51", and a minimum width of 3-1/2".  The capacity at ground shall be 23,000 lbs.  All springs shall be of center bolt design.  Cup center springs shall not be acceptable.  All spring pins shall be positively restrained from rotating in brackets and shackles.

FRONT SHOCK ABSORBERS

The front suspension system shall be equipped with Monroe, model "Magnum - 70", double acting hydraulic shock absorbers.  Shock absorbers to have a minimum bore of 1.38" and an outside diameter of approximately 3-1/4".

REAR AXLE

Rear axle assembly shall be a tandem, Meritor RT-46-160 single reduction with a capacity of 48,000 lbs.  Axles shall have a gear reduction as required.

A driver controlled inner axle lock for RT series axles shall be provided on the cab dash within easy reach of the driver.

Oil seals shall be provided as standard equipment.

REAR BRAKES

Brakes shall be "S" Cam, 16-1/2" x 7" size and shall be full air actuated with automatic slack adjusters.

REAR AXLE TOP SPEED

The rear axle/s shall be geared for a vehicle top speed in accordance with NFPA sections 4.15.2 and 4.15.3.

Units with GVWR over 26,000 pounds shall be limited to 68 mph. If the combined tank capacity is over 1250 gallons of foam and water or the GVWR is over 50,000 pounds, the vehicle top speed shall be limited to 60 mph or the fire service rating of the tires, whichever is lower.

REAR SUSPENSION

The rear suspension shall be a Hendrickson model #RT-503 with a 52" steel-walking beam and a ten (10) leaf spring pack as designed by Hendrickson Manufacturing Company. The suspension shall have a weight rating equal to the rear axle weight rating up to 48,000 pounds. Designs allowing the main pack to float are not acceptable.

BRAKE SYSTEM

A dual circuit, air operated braking system, meeting the design and performance requirements of FMVSS-121 and the operating test requirements of NFPA 1901 current edition shall be installed. It shall be direct air type with dual air treadle in the cab.  The system shall be powered by an engine mounted, gear driven air compressor protected by a heated air dryer.

The air system shall be plumbed with reinforced, air brake tubing/hose in conformance to SAE J 844-94, Type B and U.S.D.O.T. standards.  The compressor discharge shall be plumbed with stainless steel braided hose lines with a Teflon lining.  Nylon airlines shall be enclosed in high temperature convoluted loom run along the inside frame rails, secured with non-conductive, corrosion resistant strapping mounted with standoff fasteners.  Cord reinforced rubber hose lines with brass fittings shall be installed from frame rail to axle mounted air connections.

The air system shall provide a rapid air build-up feature and low-pressure protection valve with light and buzzer, designed to meet the requirements of NFPA 1901, current edition.

ABS SYSTEM

An Anti-Skid Braking System (ABS) shall be provided to improve braking control and reduce stopping distance.  This braking system shall be fitted to all of the axles.  All electrical connections shall be environmentally sealed, water, weatherproof, and vibration resistant.

The system shall constantly monitor wheel behavior during braking.  Sensors on each wheel  shall transmit wheel speed data to an electronic processor which shall sense approaching wheel lock causing  instant brake pressure modulation up to 5 times per second in order to prevent wheel lockup.  Each wheel shall be individually controlled.

To improve service trouble shooting, provisions in the system for an optional diagnostic tester shall be provided. The system shall test itself each time the vehicle is started.  A  dash-mounted light shall go out once the vehicle has attained 4 mph after successful ABS start-up To improve field performance, the system shall be equipped with a dual circuit design.  The system circuits shall be configured in a diagonal pattern.  Should a malfunction occur, the defective circuit shall revert to normal braking action.  A warning light shall signal malfunction to the operator.  The system shall consist of a wheel mounted toothed ring, sensor, sensor clip, electronic control unit and solenoid control valve.

The sensor clip shall hold the sensor in close proximity to the toothed ring.  An inductive sensor consisting of a permanent magnet with a round pole pin and coil shall produce an alternating current with a frequency proportional to wheel speed.  The unit shall be sealed, corrosion resistant and protected from electromagnetic interference.  The electronic control unit shall monitor the speed of each wheel.  A deviation shall be corrected by cyclical brake application and release.  If a malfunction occurs, the defective circuit shall signal the operator and the malfunctioning portion of the system shall shut down.  The system shall be installed in a diagonal pattern for side-to-side control.  The system shall insure that each wheel is braking to optimum efficiency up to 5 times a second.

The system shall also control application of the auxiliary engine exhaust or drive line brakes to prevent wheel lock.

This system shall have a three (3) year or 300,000 mile parts and labor warranty as provided by Meritor Wabco Vehicle Control Systems.

ELECTRONIC STABILITY CONTROL (ESC)

Electronic Stability Control (4 or 6 Channel) shall be provided as part of the Standard ABS system. The Electronic Stability Control system shall be capable of recognizing and assisting in both rollover and vehicle-under and over-steer situations through advanced monitoring of vehicle parameters and automatic and selective application of the chassis brakes. The Electronic Stability system shall use lateral and yaw accelerometers, wheel speed sensors, ABS pressure modulator valves and an ECU to control the four corners of the vehicle. The controller shall monitor the vehicle response to turning and braking, and adjust or modulate the brake pressure at the wheel end to slow the vehicle in roll control, stabilize the vehicle when under or over steering, and modulate brake pressure when excessive wheel slip, or wheel lockup is detected. By these actions, the ESC system shallhelp to maintain vehicle lateral and roll stability, improve braking and steering during heavy brake applications and braking on slippery surfaces.

AUTOMATIC TRACTION CONTROL (ATC)

To further improve vehicle drive characteristics, the unit shall be fitted with automatic traction control (ATC). This system shall control drive wheel slip during acceleration from a resting point. An extra solenoid valve shall be added to the ABS system. The system shall control the engine and brakes to ensure efficient acceleration. The system shall be equipped with a dash-mounted light indicating the ATC is controlling drive wheel slip. The system shall also include an "off road traction" dash mounted switch that will allow the operator to momentarily allow for more wheel slip when the unit is in deep mud or snow.

This system shall have a three (3) year or 300,000 mile parts and labor warranty as provided by Meritor Wabco Vehicle Control Systems.

BRAKE AIR RESERVOIRS

There shall be a minimum of four (4) air reservoirs and be installed in conformance with best automotive practices.

Reservoir capacity total shall be a minimum of 7,355 cu. in.

The air reservoirs shall be color coded to match the air lines for easy identification, ease of maintenance and troubleshooting. The reservoirs shall be painted the following colors:

- Wet Tank	Black

- Primary Tank	Green

- Secondary Tank	Blue

- Auxiliary Tank(s)	Yellow

PROTECTED AIR RESERVOIR SYSTEM

In addition to the standard air brake system, a mechanical means of releasing the spring brake shall be provided in the event of total loss of air pressure, consisting of an additional protected reservoir (1783 cu. In.), separate pressure gauge and a SR control valve on the dash.

For ease of daily maintenance, each air system reservoir shall be equipped with a brass 1/4 turn drain valve.

A Rockwell/Wabco System Saver 1200 heated air dryer shall be furnished.  An automatic moisture ejector on the primary or wet tank shall also be furnished.

AIR LINES

The entire chassis air system shall be plumbed utilizing reinforced, Synflex air lines.  All of the airlines shall be color coded to correspond with an air system schematic and shall be adequately protected from heat and chafing.

AIR COMPRESSOR

Air compressor shall be a Wabco brand, minimum of 18.7 cubic feet per minute capacity.  Air brake system shall be the quick build up type.  The air compressor discharge line shall be stainless steel braid reinforced Teflon hose.

A pressure protection valve shall be installed to prevent the use of air horns or other air operated devices should the air system pressure drop below 80 psi (552 kPa).

The chassis air system shall meet NFPA 1901, latest edition for rapid air pressure build-up within sixty (60) seconds from a completely discharged air system.  This system shall provide sufficient air pressure so that the apparatus has no brake drag and is able to stop under the intended operating conditions following the sixty (60) seconds build-up time.

BRAKE TREADLE VALVE

A Bendix dual brake treadle valve shall be mounted on the floor in front of the driver.  The brake control shall be positioned to provide unobstructed access and comfort for the driver.

PARKING BRAKE

Parking brake shall be of the spring-actuated type, mounted on the rear axle brake chambers.  The parking brake control shall be mounted on the cab center instrument panel, offset toward the driver. A red indicator light shall be provided in the driver dash panel that shall illuminate when the parking brake is applied.

AUXILIARY AIR INLET

A quick disconnect male auxiliary air inlet shall be provided at the driver's side door area at a location to be determined at a pre-construction conference.  A mating female quick disconnect female connector shall be shipped loose with the apparatus.  This shall allow a Purchaser furnished external air supply to be connected to the chassis air system.

FRONT WHEELS & TIRES

The front wheels shall be 22.5" x 12.25" ten stud, hub piloted polished aluminum disc type.

The aluminum disc front wheels shall be provided with bright nut covers and hub caps.

FRONT TIRES

The front tires shall be Michelin 425/65R22.5 "20 Ply" tubeless radial XZY3 wide base mixed tread.  The tires shall be fire service rated up to 24,400 lbs and shall have a top speed of 65 mph when inflated to 120 psi.

Fire Service Rating means operations not to exceed one hour loaded travel at maximum speed, with at least a one hour cool down prior to another loaded run.

Industry load and inflation standards are in a constant state of change.  Printed material may not reflect the latest load and inflation standards.

NOTE: NEVER EXCEED THE MAXIMUM AIR PRESSURE LIMITATION

REAR WHEELS

The tandem rear axle wheels shall be 22.5" x 9" ten stud, hub piloted polished aluminum disc type.

The tandem rear aluminum disc wheels shall be provided with bright nut covers and hub caps.

REAR TIRES

The rear tires shall be Michelin 315/80R22.5 "20 Ply" tubeless radial XZA1 traction tread.  The tires shall be fire service rated up to 70,000lbs and shall have a top speed of 75 mph when inflated to 130 psi.

Fire Service Rating means operations not to exceed one hour loaded travel at maximum speed, with at least a one hour cool down prior to another loaded run.

Industry load and inflation standards are in a constant state of change.  Printed material may not reflect the latest load and inflation standards.

NOTE: NEVER EXCEED THE MAXIMUM AIR PRESSURE LIMITATION

TIRE PRESSURE MONITORING DEVICES

Each tire shall be equipped with an air pressure indicator cap on the valve stem. Each cap shall have a visual indicator to show if the tire is correctly inflated.

ENGINE

IMPORTANT NOTICE:

You have chosen a “2007 emission compliant” diesel engine equipped chassis; this engine is subject to availability on hand at the time of order of apparatus from Kovatch Mobile Equipment. Time of order means date of acceptance by KME of a valid purchase order or written sales contract with a fully completed order entry package, and the return of an order acknowledgement letter from KME, which includes an assigned General Shop Order Number (“GSO #”) and Sales Engineer. This confirmation must expressly state that the engine selection is confirmed and will be included in your order. Based on impending 2010 EPA federal emission changes, the 2007 emission compliant engines are in limited supply and inventory can/may be depleted at any point in time.

If at time of order from KME the selected engine is no longer available, KME cannot be held responsible for nor participate in any additional costs resulting from modification of the order to provide a viable and available engine offering. These costs could include, but are not limited to, changing engine manufacturer, horsepower, or upgrading to a 2010 emission compliant engine or commercial chassis. Additional engine order content, and related costs, could be affected if a different 2007 EPA emission compliant engine is required to be substituted due to unavailability of the selected engine. These costs may also include those resulting from required changes in associated order option content necessitated by substitution of an alternative engine. Such charges could include but are not limited to changing the transmission model or cab type. KME will work with each customer in an effort to minimize changes while meeting the customer’s requirements and specifications as closely as possible.

PLEASE NOTE:  IT IS POSSIBLE THAT AN ENGINE SHORTAGE WILL OCCUR FOR THE 2010 MODEL YEAR, WHICH MAY RESULT IN A DELAY IN PRODUCTION OF SOME 2010 MODEL YEAR VEHICLES.  KME IS MAKING EVERY REASONABLE EFFORT TO AVOID SUCH A DELAY, BUT IS NOT RESPONSIBLE FOR ANY ACTUAL DELAY THAT OCCURS AS THE DIRECT RESULT OF AN ENGINE SHORTAGE.

Any other written or verbal statements, agreements or representations made regarding 2007 emission compliant engines or their availability are superseded by the foregoing statements regarding the sale and availability of 2007 EPA emission compliant engines by KME.

ENGINE

Engine shall be a Cummins, Model ISM 500, diesel, turbo-charged, per the following specifications.

- Max. Horsepower	500 HP @ 1900 RPM

- Governed Speed	2100 RPM

- Peak Torque	1550 lb. ft. @ 1200 RPM

- Cylinders	Six (6)

- Operating Cycles	Four (4)

- Bore & Stroke	4. 9 x 5.8 in.

- Displacement	661 cu. in.

- Compression Ratio	16.1:1

- Governor Type	Limiting Speed

- Drive line Size	1810 Series

Engine oil filters shall be engine manufacturers branded or approved equal. Engine oil filters shall be accessible for ease of service and replacement.

A fuel/water separator shall be provided.

The manufacturer shall be able to furnish proof of engine installation approval by the engine manufacturer.

ENGINE WARRANTY

The Cummins engine shall be warranted for a period of five (5) years or 100,000 miles, whichever occurs first.

COOLING/RADIATOR

Radiator shall be brass with bolted steel top and bottom tanks. The cooling system shall be designed for a maximum of fifteen (15) PSI operation. There shall be a sight glass in the radiator to check the coolant level without removing the radiator cap. The core construction shall be tube and fin with three (3) tube rows, 273 total core tubes, and fourteen (14) fins per inch.

Extended life engine coolant shall provide anti-freeze protection to -30° F. The mixture shall be per the engine manufacture's specifications.

A transmission oil to liquid cooler shall be furnished.

Core area shall be a minimum of 1375 square inches (39 H x 35.25W).

RADIATOR SKID PLATE

The radiator installation shall include a heavy-duty radiator skid plate to protect the radiator from debris or obstructions under the chassis.  The skid plate shall be designed so the angle of approach is not affected.

CHARGE AIR COOLER

The charge air cooler shall be constructed of aluminum with cast aluminum side tanks. The cooler shall have a frontal core size of 957 square inches, seven (7) fins per inch, and forty eight (48) core tubes.

The charge air cooler shall be mounted directly ahead of the radiator and to the radiator headers. Rubber isolators shall be used at the mounting points to reduce transmission of vibrations.

The piping between the charge air cooler and engine shall use heavy duty hoses with stainless steel bands. Bands are used to maintain the shape of the hose during changing turbo boost pressures. The hoses shall be attached with stainless steel constant torque hose clamps.

COOLING SYSTEM FAN

The engine cooling system shall incorporate a heavy duty fan, installed on the engine and include a shroud.

The fan shall be equipped with an air operated clutch fan, which shall activate at a pre-determined temperature range.

Re-circulation shields shall be installed to ensure that air which has passed through the radiator is not drawn through it again.

COOLANT OVERFLOW RECOVERY SYSTEM

A one and one-half (1-1/2) gallon coolant recovery system shall be provided, located inside the engine enclosure and shall be accessible from the access hatch located at the rear of the engine enclosure.

Heavy duty silicone heater and coolant hoses shall be furnished for the heater and coolant system. All coolant hoses shall be equipped with constant torque type hose clamps. All integral hoses supplied with the engine shall be as supplied by the engine manufacturer.

LOW COOLANT INDICATOR LIGHT AND ALARM

A low engine coolant indicator light located in the dash instrument panel shall be provided.  An audible alarm shall be provided to warn of the low coolant condition.

ENGINE BRAKE

An engine compression brake shall be furnished for increased braking capabilities.  Controls shall be as provided by the engine manufacturer and shall be activated by releasing the throttle pedal to the idle position.

The engine compression brake shall have dash mounted control switches to turn the brake on or off as well as to control the operational level of the brake.

The engine brake shall be wired in such a manner so as to illuminate the chassis brake lights when the engine brake is engaged and operating.

The engine brake shall be interlocked with the PTO operation and shall automatically disengage any time the apparatus is operating with the PTO active.

ENGINE FAST IDLE

A fast idle for the electronic controlled engine shall be provided.  The fast idle shall be controlled by an ON/OFF switch on the dash.

An electronic interlock system shall prevent the fast idle from operating unless the transmission is in "Neutral" (or "Park" if so equipped) and the parking brake is fully engaged.  If the fast idle control is used in conjunction with a specified engine/transmission driven component or accessory, the fast idle control shall be properly interlocked with the engagement of the specified component or accessory.

AIR CLEANER

An engine air cleaner shall be provided. Air cleaner shall include a dry type element.  Air cleaner shall be installed in accordance with the engine manufacturer's recommendations. The air cleaner shall be located to the rear of the engine, with streamline air pipes and hump hose connections from the inlet to the air cleaner and from the air cleaner to the turbo. The air cleaner shall be easily accessible when the cab is tilted.

Air cleaners mounted on the side or near the bottom of the cab shall not be acceptable. [NO EXCEPTIONS]

SPARK ARRESTOR

A spark arrestor shall be installed in the chassis air intake system. This arrestor shall be mounted behind the intake grille to filter out airborne embers. The spark arrestor housing must be easily accessible when the cab is tilted.

ACCELERATOR CONTROL

A floor mount accelerator pedal shall be installed on the floor in front of the driver. The pedal shall be positioned for comfort with ample space for fire boots and adequate clearance from the brake pedal control.

TRANSMISSION

An Allison World Transmission, Model 4000 EVS electronically controlled, automatic transmission shall be provided.  Transmission specifications shall be as follows:

- Max. Gross Input Power	600 HP

- Max. Gross Input Torque	1850 lb. ft.

- Input Speed (Range)	1700- 2300 RPM

- Shift Calibrations	5 Speed (6th not avail. for fire appl.)

- Direct Gear (Pumping)	4th (Lock-up)

- Direct Gear Ratio	1.00:1

- Overdrive Ratio	0.74:1

Transmission installation shall be in accordance with the transmission manufacturer's specification.  The transmission shall be readily and easily removable for repairs or replacement.

TOUCH PAD TRANSMISSIOIN CONTROL

An illuminated, touch-pad type shift control shall be mounted in the cab, convenient to the driver.  Shift control shall be approved by the transmission manufacturer.

TRANSMISSION OIL LEVEL SENSOR

The transmission shall be equipped with the oil level sensor (OLS); this sensor shall allow the operator to obtain an indication of the fluid level from the shift selector. The sensor display shall provide the following checks, correct fluid level, low fluid level and high fluid level.

PARK TO NEUTRAL

The transmission, upon application of the parking brake, shall automatically shift into neutral.

SYNTHETIC TRANSMISSION FLUID

Castrol "TRANSYND" or an equivalent synthetic TES 295 transmission fluid shall be utilized to fill the 4000 EVS transmission.

DRIVE LINES

Drive lines shall be Dana (Spicer) 1810 heavy duty series or equal, with "glide coat" splines on all slip shafts.  The chassis manufacturer shall utilize an electronic type balancing machine to statically and dynamically balance all drive shafts.  The chassis manufacturer shall be able to provide proof of compliance with all drive shaft manufacturer's standards and specifications.  (No Exceptions)

EXHAUST SYSTEM

The exhaust system shall be installed in accordance with the engine manufacturer's requirements and meet all Cummins Non - DPF system requirements and State noise level requirements.  Exhaust system components shall be securely mounted and easily removable.

The muffler shall be sized to be compatible with the engine exhaust discharge.

Exhaust tubing shall be a minimum of 16 gauge material.  Any flexible exhaust tubing shall be HDT stainless steel type. To minimize heat build-up, exhaust tubing within the engine compartment shall be wrapped with an insulating material. Exhaust shall be wrapped from the turbocharger to the entrance of the muffler. Material shall be held in place with worm gear type clamps.

The exhaust tailpipe extending from the muffler (DPF) to  the side of the vehicle shall be constructed from 16-gauge aluminized steel tubing.  The exhaust discharge shall be on the right side of the apparatus forward of the rear axle.

FUEL TANK

Fuel tank shall be a minimum of sixty-five (65) gallon capacity.  It shall have a minimum fuel filler neck of 2" ID.  A 1/2" minimum diameter drain plug shall be provided.  The tank shall be fabricated from hot rolled, pickled and oiled steel.  Provisions for an additional feed line and fuel level float shall be provided for apparatus manufacturer's use.

The fuel tank shall be installed behind the rear wheels between the frame rails.

The fuel tank shall meet all FHWA 393.67 requirements including a fill capacity of 95% of tank volume.

The fuel lines shall be wire braid reinforced fuel hose.  The lines shall be carefully routed and secured along the inside of the frame rails.

FUEL COOLING SYSTEM

A fuel cooling system shall be provided.  The heat exchanger shall be a tube and fin type and shall be a separate unit.  The cooler shall be mounted forward of the radiator and plumbed to the fuel return line.

FUEL FILTER/WATER SEPARATOR

A Racor heated fuel filter/water separator shall be provided in the fuel system. A "water in fuel" indicator shall be provided on the dash.

SECONDARY ELECTRIC FUEL PUMP

In addition to the primary fuel pump, a secondary electric fuel pump for re-priming shall be furnished in the main fuel line.  A labeled control switch shall be provided on the main dash panel.

FUEL POCKET

A fuel fill shall be provided in the left side rear wheel well area.  A Cast Products heavy duty cast aluminum spring loaded hinged fill door shall be provided.

A label indicating "Ultra Low Sulfur Diesel Fuel Only" shall be provided adjacent to the fuel fill.

FUEL FILL PANEL

A polished stainless steel trim panel shall be provided around the fuel fill door on the side of the body panel.

DUAL POWER STEERING

A dual power steering system shall be provided utilizing a Sheppard Model #M110 main steering gear on the driver side of the chassis and a Sheppard model #M90 assist steering gear on the officer side of the chassis.

The power steering gear on the officer side of the chassis will increase performance in turning the officer side wheel assembly, reducing loads and forces on the main gear and components.

The steering system shall be designed to maximize the turning capabilities of the front axle no matter the rating and tire size. The use of a power assist cylinder on the officer side of the chassis is NOT ACCEPTABLE.

The system shall be designed utilizing an engine driven hydraulic pump, with a maximum operating pressure of 2000 PSI. Steering design shall permit a maximum of 5.6 turns from stop to stop. Steering system components shall be mounted in accordance with the steering gear manufacturer's instructions.

STEERING WHEEL

The steering wheel shall be vinyl padded, minimum 18" diameter, with a center hub mounted horn button.  There shall be a self-canceling, directional signal lever and a traffic hazard switch on the steering column.  The high beam activator shall be controlled by pulling the directional signal lever toward the driver.

The steering column shall have a separate lever control for tilting and telescoping capability.

ROAD SAFETY KIT

A road safety kit shall be furnished with the following equipment:

- 2 1/2 lb. B-C fire extinguisher

- Triangle safety reflectors

CHASSIS ELECTRICAL SYSTEM

All electrical wiring in the chassis shall be SXL cross link insulated type. Wiring is to be color coded and include function codes every three (3) inches on both sides. Wiring harnesses shall be routed in protective, heat resistant loom, securely and neatly installed. Two (2) power distribution centers shall be provided in central locations for greater accessibility.  The power distribution centers shall contain automatic thermal self resetting breakers, power control relays, flashers, diode modules, daytime driving light module, and engine and transmission data links.  All breakers and relays shall have a capacity substantially greater than the expected load on the related circuit, thus ensuring long component life.  Power distribution centers shall be composed of a system of interlocking plastic modules for ease of custom construction.

The power distribution centers shall be function oriented. The first is to control major truck function. The second control center shall enable overhead switching and interior operations. Each module shall be single function coded and labeled to aid in troubleshooting.  The centers shall also have accessory breakers and relays for future installations.  All harnesses and power distribution centers shall be electrically tested prior to installation to ensure the highest system reliability.

All external harness interfaces shall be of a triple seal type connection to ensure a proper connection.  The cab/chassis and the chassis/body connection points shall be mounted in accessible locations.  Complete chassis wiring schematics shall be supplied with the apparatus.

WIRING HARNESS DESCRIPTION

The wiring harness contained on the chassis shall be designed to utilize wires of stranded copper or copper alloy of a gauge rated to carry 125% of maximum current for which the circuit is protected without exceeding 10% voltage drop across the circuit.  Wiring must be uniquely identified by color code or circuit function code, labeled at a minimum of every three (3) inches.  The identification of the wiring shall be referenced on a wiring diagram.  All wires conform to SAEJ1127 (Battery Cable), SAEJ1128 (Low Tension Primary Cable), SAEJ1560 (Low Tension Thin Wall Primary Cable).

The covering of harnesses shall be moisture resistant loom with a minimum rating of 289 Degrees Fahrenheit and a flammability rating of VW-1 as defined in UL62.  The covering of jacketed cable shall have a minimum rating of 289 degree Fahrenheit.

All harnesses must be securely installed in areas protected against heat, liquid contaminants and damage.  The harness connections and terminations shall use a method that provides a positive mechanical and electrical connection and are in accordance with the device manufacturer's instructions.  No connections within the harness may utilize wire nut, insulation displacement, or insulation piercing components.

All circuits shall conform to SAEJ1292.  All circuits must be provided with low voltage over current protective devices.  These devices shall be readily accessible and protected against heat in excess of component rating, mechanical damage, and water spray.  Star washers shall not used for ground connections.

DIRECT GROUNDING STRAPS

Direct grounding straps shall be mounted to the following areas; frame to cab, frame to body and frame to pump enclosure.

All exposed electrical connections shall be coated with "Z-Guard 8000" to prevent corrosion.

EMI/RFI PROTECTION

The apparatus shall incorporate the latest designs in the electrical system with state of the art components to insure that radiated and conducted electromagnetic interference (EMI) and radio frequency interference (RFI) emissions are suppressed at the source

The apparatus proposed shall have the ability to operate in the environment typically found in fire ground operations with no adverse effects from EMI/RFI.

EMI/RFI susceptibility is controlled by utilizing components that are fully protected and wiring that utilizes shielding and loop back grounds where required.  The apparatus shall be bonded through wire braided ground straps.  Relays and solenoids that are suspect to generating spurious electromagnetic radiation are diode protected to prevent transient voltage spikes

In order to fully prevent the radio frequency interference the purchaser may be requested to provide a listing of the type, power output, and frequencies of all radio and bio medical equipment that is proposed to be used on the apparatus.

12 VOLT ELECTRICAL SYSTEM TESTING

The apparatus low voltage electrical system shall be tested and certified by the apparatus manufacture.  The certification shall be provided with the apparatus.  All tests shall be performed with air temperature between 0°F and 100°F.

The following three (3) tests shall be performed in order.  Before each test, the batteries shall be fully charged.

TEST #1-RESERVE CAPACITY TEST

The engine shall be started and kept running until the engine and engine compartment temperatures are stabilized at normal operating temperatures and the battery system is fully charged.  The engine shall be shut off and the minimum continuous electrical load shall be activated for 10 minutes.  All electrical loads shall be turned off prior to attempting to restart the engine.  The battery system shall then be capable of restarting the engine.  Failure to restart the engine shall be considered a test failure.

TEST #2-ALTERNATOR PERFORMANCE TEST AT IDLE

The minimum continuous electrical load shall be activated with the engine running at idle speed.  The engine temperature shall be stabilized at normal operating temperature.  The battery system shall be tested to detect the presence of battery discharge current.  The detection of battery discharge current shall be considered a test failure.

TEST #3-ALTERNATOR PERFORMANCE TEST AT FULL LOAD

The total continuous electrical load shall be activated with the engine running up to the engine manufacturers governed speed.  The test duration shall be a minimum of 2 hours.  Activation of the load management system shall be permitted during this test.  However, an alarm sounded due to excessive battery discharge, as detected by the system, or a system voltage of less than 11.7 volts DC for a 12 volt system, for more than 120 seconds, shall be considered a test failure.

LOW VOLTAGE ALARM TEST

Following completion of the preceding tests, the engine shall be shut off.  The total continuous electrical load shall be activated and shall continue to be applied until the excessive battery discharge alarm is activated.

The battery voltage shall be measured at the battery terminals.  With the load still applied, a reading of less than 11.7 volts shall be considered a test failure.  The battery system shall then be able to restart the engine.

At time of delivery, documentation shall be provided with the following information:

- Documentation of the electrical system performance test

- A written load analysis of the following;

- Nameplate rating of the alternator

- Alternator rating at idle while meeting the minimum continuous electrical load

- Each component load comprising the minimum continuous electrical load.

- Additional loads that, when added to the minimum continuous load, determine the total connected load.

- Each individual intermittent load.

LOAD MANAGEMENT SYSTEM

A load management system shall be provided for performing electrical load management.  The load manager shall have 16 programmable outputs to supply warning and load switching requirements.  The load management system shall be capable of offering load sequencing, load shedding, fast idle control, low voltage warning, scene mode operation and response mode operation

Outputs 1 thru 12 shall be independently programmable to activate during the scene mode, the response mode or both. These outputs can also be programmed to activate with the ignition or master warning switch, or to sequence and shed along with the priority. Output 13 shall be designated to activate a fast idle system. Output 14 shall provide a low voltage warning for an isolated battery.  Output 15 is a user configurable output and shall be programmable for activating between 10.5 and 15 volts. Output 16 shall provide a low voltage alarm that activates at the NFPA required 11.8 volts.

The load management shall have a digital display to indicate system voltage in normal operation mode and also indicate the output configuration during programming mode.

The load management shall also be protected against reverse polarity and shorted outputs, and be enclosed in a metal enclosure to enhance EMI/RFI protection.

DIAGNOSTICS

Diagnostic ports shall be accessible while standing on the ground and located inside the drivers side door left of the steering column. The diagnostic panel shall allow diagnostic tools such as computers to connect to various vehicle systems for improved troubleshooting providing a lower cost of ownership. Diagnostic switches shall allow engine and ABS systems to provide blink codes should a problem exist.

The diagnostic system shall include the following:

- Engine diagnostic port

- Transmission and ABS diagnostic port

- Roll sensor diagnostic port (if applicable)

Additional diagnostic locations under the officers side of the dash.

- Engine diagnostic switch (blink codes)

- ABS diagnostic switch (blink codes)

VOLTAGE MONITOR SYSTEM

A voltage monitoring system shall be provided to indicate the status of the battery system connected to the vehicle's electrical load.  The system shall provide visual and audible warning when the system voltage is below or above optimum levels.

The alarm shall activate if the system falls below 11.8 volts DC for more than two (2) minutes.

INDICATOR LIGHT AND ALARM PROVE-OUT SYSTEM

A system shall be provided which automatically tests basic indicator lights and alarms located on the cab instrument panel.

SEQUENCER

A sequencer shall be provided that automatically activates and deactivates vehicle loads in a preset sequence thereby protecting the alternator from power surges. This sequencer operation shall allow a gradual increase or decrease in alternator output, rather than loading or dumping the entire 12 volt load to prolong the life of the alternator.

Emergency light sequencing shall operate in conjunction with the emergency master light switch. When the emergency master switch is activated, the emergency lights shall be activated one by one at half second intervals.  Sequenced emergency light switch indicators shall flash while waiting for activation.

When the emergency master switch is deactivated, the sequencer shall deactivate the warning light loads in the reverse order.

Rear of cab Air-Conditioning and Heat shall be load managed.

ELECTRICAL HARNESS REQUIREMENT

To ensure dependability, all 12-volt wiring harnesses installed by the apparatus manufacturer shall conform to the following specifications:

- SAE J 1128 - Low tension primary cable

- SAE J 1292 - Automobile, truck, truck-tractor, trailer and motor coach wiring

- SAE J 163 - Low tension wiring and cable terminals and splice clips

- SAE J 2202 - Heavy duty wiring systems for on-highway trucks

- NFPA 1901 - Standard for automotive fire apparatus

- FMVSS 302 - Flammability of interior materials for passenger cars, multipurpose passenger vehicles, trucks and buses

- SAE J 1939 - Serial communications protocol

- SAE J 2030 - Heavy-duty electrical connector performance standard

- SAE J 2223 - Connections for on board vehicle electrical wiring harnesses

- NEC - National Electrical Code

- SAE J 561 - Electrical terminals - Eyelet and spade type

- SAE J 928 - Electrical terminals - Pin and receptacle type A

For increased reliability and harness integrity, harnesses shall be routed throughout the cab and chassis in a manner which allows the harnessing to be laid into it's mounting location.  Routing of harnessing which requires pulling of wires through tubes shall not be allowed.

Wiring shall be run in loom or conduit where exposed, and have grommets or other edge protection where wires pass through metal.  Wire colors shall be integral to each wire insulator and run the entire length of each wire. Harnessing containing multiple wires and uses a single wire color for all wires shall not be allowed.  Function and number codes shall be continuously imprinted on all wiring harness conductors at 3.00" intervals.  All wiring installed between the cab and into doors shall be protected by a wire conduit to protect the wiring.  Exterior exposed wire connectors shall be positive locking, and environmentally sealed to withstand elements such as temperature extremes, moisture and automotive fluids.  Electrical wiring and equipment shall be installed utilizing the following guidelines:

- All holes made in the roof shall be caulked with silicon (no exception).  Large fender washers, liberally caulked, shall be used when fastening equipment to the underside of the cab roof.

- Any electrical component that is installed in an exposed area shall be mounted in a manner that shall not allow moisture to accumulate in it.  Exposed area shall be defined as any location outside of the cab or body.

- For low cost of ownership, electrical components designed to be removed for maintenance shall be quickly accessible.  For ease of use, a coil of wire shall be provided behind the appliance to allow them to be pulled away from the mounting area for inspection and service work.

- Corrosion preventative compound shall be applied to non-waterproof electrical connectors located outside of the cab or body.  All non-waterproof connections shall re-quire this compound in the plug to prevent corrosion and for easy separation of the plug.

- Any lights containing non-waterproof sockets in a weather-exposed area shall have corrosion preventative compound added to the socket terminal area.

- All electrical terminals in exposed areas shall have protective coating applied completely over the metal portion of the terminal.

- Rubber coated metal clamps shall be used to support wire harnessing and battery cables routed along the chassis frame rails.

- Heat shields shall be used to protect harnessing in areas where high temperatures exist.  Harnessing passing near the engine exhaust shall be protected by a heat shield.

- Cab and crew cab harnessing shall not be routed through enclosed metal tubing.  Dedicated wire routing channels shall be used to protect harnessing therefore improving the overall integrity of the vehicle electrical system. The design of the cab shall allow for easy routing of additional wiring and easy access to existing wiring.

- All standard wiring entering or exiting the cab shall be routed through sealed bulkhead connectors to protect against water intrusion into the cab.

BATTERY CABLE INSTALLATION

All 12-volt battery cables and battery cable harnessing installed by the apparatus manufacturer shall conform to the following requirements:

- SAE J 1127 - Battery Cable

- SAE J 561 - Electrical terminals, eyelets and spade type

- SAE J 562 - Nonmetallic loom

- SAE J 836 A - Automotive metallurgical joining

- SAE J 1292 - Automotive truck, truck-tractor, trailer and motor coach wiring

- NFPA 1901 - Standard for automotive fire apparatus

Battery cables and battery cable harnessing shall be installed utilizing the following guidelines:

- Splices shall not be allowed on battery cables or battery cable harnesses.

- For ease of identification and simplified use, battery cables shall be color coded.  All positive battery cables shall be marked red in color.  All negative battery cables shall be black in color.

- For ease of identification, all positive battery cable isolated studs throughout the cab and chassis shall be red in color.

- For increased reliability and reduced maintenance, all electrical buss bars located on the exterior of the apparatus shall be coated to prevent corrosion.

An operational test shall be conducted to ensure that any equipment that is permanently attached to the electrical system is properly connected and in working order.

ALTERNATOR

The alternator shall be Leece Neville Model 4890JB, 320 amp, serpentine belt driven unit.  The installation shall include an integral self-diagnostic regulator and rectifier for compact installation.

The alternator installation shall be designed to provide maximum output at engine idle speed to meet the minimum continuous electrical load of the apparatus as required.

BATTERY SYSTEM

Five (5) Group 31, maintenance free batteries shall be provided.  Each battery shall be rated at 925 CCA at 0° F.  Reserve capacity shall be 180 minutes.  Wiring for the batteries shall be 4/0 welding type dual path starting cables for SAEJ541.

BATTERY STORAGE

Batteries shall be securely mounted in fixed stainless steel trays located on each side of the chassis frame.  Complete access shall be provided when the cab is fully tilted.  Batteries shall be mounted on non-corrosive matting material.

BATTERY DISCONNECT SWITCH

The chassis batteries shall be wired in parallel to a single 12 volt electrical system, controlled through a heavy duty, rotary type, master disconnect switch.  The master disconnect switch shall be located within easy access of the driver upon entering or exiting the cab.

BATTERY JUMPER STUDS

A set of Cole Hersee battery jumper studs, Model #46210-02 (red) and #46210-03 (black) shall be provided to allow the battery system to be jump started or charged from an external source.  The studs shall be located on the bottom of the battery box on the driver's side of the chassis. Each stud shall be equipped with rubber protector caps.

120 VOLT SHORELINE CONNECTION - "SUPER" AUTO EJECT

One (1) Kussmaul "Super" Auto Eject Model  091-55-20-120, automatic, 120 volt, 20 amp shoreline disconnect shall be provided for the on board, 110 volt battery charging systems.

The disconnect shall be equipped with a NEMA 5-20 P male receptacle, which shall automatically eject the shoreline when the vehicle starter is energized.  A label shall be provided indicating voltage and amperage ratings.

SHORELINE POWER INLET PLATE

A shoreline power receptacle information plate shall be permanently affixed at or near the power inlet.  The plate shall indicate the following;

- Type of Line Voltage

- Current Rating in Amps Power Inlet Type (DC or AC)

The Kussmaul auto-eject connection shall be equipped with a Red weatherproof cover.

The shoreline receptacle shall be located in the area directly adjacent to the driver's side cab door, above the side air grille.

BATTERY CHARGER / AIR COMPRESSOR SYSTEM

A Kussmaul model #091-9-1200, "Pump Plus 1200"  air compressor/high output battery charger shall be provided for maintaining the vehicle's air / battery system.  Unique electronic sensing circuits sense the true battery voltage while eliminating the need for external sense wires.  Output current shall be 40 amperes @ 12 volt DC. 

	The air compressor shall maintain the air pressure in the chassis air brake system while the vehicle is not in use. The air compressor shall have a rated input at 12 volt DC @ 12 amps and an output of 0.30 SCFM @ 80 psi.

An LED bar graph display shall be located near the shoreline connection to monitor the battery status.

EMERGENCY SWITCHES

A switch control console shall be provided in the center dash panel between the driver's and officer's position.  This console shall separate the emergency / auxiliary electrical functions from the regular chassis functions.  A minimum of ten (10) rocker type switches with integral indicator lights shall be provided, in addition to the Load Manager indicator.

A master switch with integral red indicator light shall be provided, which shall allow pre-setting of emergency light switch and shall have a red integral indicator light.  A primary emergency lighting switch shall be provided, next to the master switch.  Then a total of seven (7) load manageable emergency switches shall be provided.  The last remaining switch shall be a ground light switch.  All switches, (other than the master switch), shall have switch function labeling and an amber integral indicator light.

LIGHTING - CAB INTERIOR

Four (4) combination red/white dome lights shall be furnished in the cab, two (2) in the forward section and two (2) in the rear section.  The lights shall be Weldon model #8086-6978-68 with euro style switch.  Each dome light shall have an integral selector switch.  Each dome light shall also activate when the respective, adjacent cab door is opened.

A shielded light shall be provided in each side opening, cab door step well.  These lights shall activate with the respective door jamb switch.

"DO NOT MOVE APPARATUS" WARNING LIGHT WITH AUDIBLE ALARM

A red flashing warning light with an integral audible alarm, shall be functionally located in the cab to signal when an unsafe condition is present such as an open cab door or body compartment door, an extended ladder rack, a deployed stabilizer, an extended light tower or any other device which is opened, extended or deployed which may cause damage to the apparatus if it is moved.

This light shall be activated through the parking brake switch to signal when the parking brake is released. This light shall be labeled "DO NOT MOVE APPARATUS WHEN LIGHT IS ON".

CIGARETTE LIGHTER PORT

One (1) 12 volt cigarette lighter style accessory outlet(s) shall be installed in the cab of the truck for the fire departments accessory devices. The lighter(s) shall be located as directed near the officer's seating position for devices such as cellular phones.

12 VOLT ACCESSORY CIRCUIT - CAB DASH

Eight (8) dedicated 12 volt power and ground circuit shall be provided in the cab dash (4) and overhead console (4). The circuit shall be for future installation of radios or accessories.

12 VOLT ACCESSORY CIRCUIT - CREW CAB AREA

A dedicated 12 volt power and ground circuit shall be provided in the rear crew area as required. The circuit shall be for future installation of radios or accessories.

HEADLIGHTS CLUSTER

Two (2) dual, rectangular, halogen headlight modules in bright finish bezels shall be furnished on the front of the cab.  Each head light module shall incorporate an individual low beam and a high beam headlight.  High beam actuation shall be controlled on the turn signal lever.

DAYTIME RUNNING LIGHTS

The chassis head lights shall have integrated circuitry to actuate the low beam headlights at a maximum of 80 percent of capacity whenever the chassis engine is running.

The daytime running lights shall be interlocked with the parking brake.

SECONDARY DUAL LIGHT MODULE

Two (2) Whelen 60 A 00 TAR arrow shaped, amber LED turn signals shall be provided, one (1) in each side of the dual light module above the headlights.

The NFPA required, Zone "A" lower warning lights shall be incorporated into each side dual light module noted above.

DOT MARKER LIGHTS AND REFLECTORS

Five (5) DOT approved Whelen (or equal) Light Emitting Diode (LED) cab marker lamps shall mounted on the top front edge of the cab roof.

Truck-Lite Model 18 amber LED marker lights/auxiliary turn signals with integral reflectors shall be provided on the side of the cab above the front wheel well, one (1) each side.

Truck-Lite Model #18 red LED marker lights with integral reflectors shall be provided at the lower side rear, one (1) each side.

Truck-Lite #60115Y yellow LED side marker and turn lights shall be provided on the apparatus lower side, forward of rear axle, one (1) each side.

Truck-Lite Model #19 red LED clearance lights shall be provided on the apparatus rear upper, one (1) each side at the outermost practical location.

Truck-Lite Model #33740R LED 3-lamp identification bar will be provided on the apparatus rear center.  The lights shall be red in color.

Truck-Lite #98034Y yellow reflectors shall be provided on the apparatus body lower side, as far forward and low as practical, one (1) each side if the apparatus is 30' long or longer.

Truck-Lite #98034R red reflectors shall be provided on the apparatus rear, one (1) each side at the outermost practical location.

LICENSE PLATE LIGHT - REAR

One (1) license plate light shall be provided above the mounting position of the license plate.  The light shall be clear in color.

TAIL, STOP, TURN AND BACK-UP LIGHTS

Two (2) Whelen 600 series, 4-1/8" x 6-1/2", LED red combination tail and stop lights, shall be mounted one each side at the rear of the body.

Two (2) Whelen 600 series, 4-1/8" x 6-1/2", LED amber arrow turn signal lights, shall be mounted one each side, on a vertical plane with the tail/stop lights.

Two (2) Whelen 600 series, 4-1/8" x 6-1/2", LED white back-up lights, shall be mounted one each side on a vertical plane with the turn/tail/stop signals.  These lights shall activate when the transmission is placed in reverse gear.

Two (2) Whelen PLAST4V mounting flanges, installed one (1) on each side, shall be provided to mount the lights described above in one common mounting flange.  The fourth opening shall be for the lower rear warning lights.

CAB STEP LIGHTS

Chrome plated Whelen Model #T0C0ACCR, shielded LED chassis step lights shall be provided and controlled with marker light actuation. The lights shall be surface mounted using Whelen #TFLANGEC, chrome plated flange.  Step lights shall be located to properly illuminate all  chassis access steps and walkway areas.

BODY STEP LIGHTS

Chrome plated Whelen Model #0AC0EDCR, shielded LED body step lights shall be provided and controlled with marker light actuation.  Step lights shall be located to properly illuminate all  chassis access steps and walkway areas.

DUNNAGE AREA LIGHTING

Two (2) chrome plated Whelen Model #0AC0EDCR, shielded LED lights shall be provided in the dunnage area to provide adequate illumination of this area.

DECK LIGHTS / WORK LIGHTS

Two (2) 6" Unity model AG chrome plated deck lights shall be provided and mounted on the rear stanchions, one (1) each side.  Each individual deck light shall be controlled by an individual switch mounted on each light, as well as by a single master switch in the master warning switch console.

The deck lights shall also serve as rear work lights to illuminate the rear of the apparatus to meet NFPA-1901 requirements.

GROUND LIGHTS - CAB

One (1) Truck-Lite Model 44 LED ground light shall be provided under each side cab door entrance step, four (4) total. The ground lights shall turn on automatically with each respective door jamb switch and also by a master ground light switch in the warning light switch console.

Each light shall illuminate an area at a minimum 30" outward from the edge of the vehicle. The rear crew door ground lights shall be positioned at an angle rearward to provide illumination at the pump panel and the front of the body work areas.

GROUND LIGHTS - PUMP PANEL

One (1) Truck-Lite Model 44 LED ground light shall be provided under each side pump panel running board, two (2). The ground lights shall be activated by a master ground light switch in the cab and shall be wired through the load management system.

GROUND LIGHTS - MIDSHIP

One (1) Truck-Lite Model 44 LED ground light shall be provided under each midship compartment, total of two (2). The ground lights shall be activated by a master ground light switch in the cab and shall be wired through the load management system.

GROUND LIGHTS - REAR

One (1) Truck-Lite Model 44 LED ground light shall be provided under each rear body corner, two (2) total. The ground lights shall be activated by a master ground light switch in the cab and shall be wired through the load management system.

GROUND LIGHT SWITCHING

The cab and body ground lights shall activate by engaging the parking brake.

12 VOLT BODY ELECTRICAL SYSTEM

All electrical lines in the body shall be protected by automatic circuit breakers, conveniently located to permit ease of service. Flashers, heavy solenoids and other major electrical controls shall be located in a central area near the circuit breakers.

All lines shall be color and function coded every 3", easy to identify, oversized for the intended loads and installed in accordance with a detailed diagram. A complete wiring diagram shall be supplied with the apparatus.

Wiring shall be carefully protected from weather elements and snagging.  Heavy duty loom shall be used for the entire length. Grommets shall be utilized where wiring passes through panels.

In order to minimize the risk of heat damage, wires run in the engine compartment area shall be carefully installed and suitably protected by the installation of heat resistant shielded loom.

All electrical equipment shall be installed to conform to the latest federal standards as outlined in NFPA 1901.

BODY ELECTRICAL JUNCTION COMPARTMENT

A weather resistant electric junction compartment shall be provided in the left side lower front compartment. This compartment shall be recessed through the inside rear wall of the compartment to provide an easily accessible enclosure to house all of the body wiring junction points, terminal strips, solenoids, etc. The design of this compartment shall not decrease the storage capacity area of the compartment in which it is located. A removable panel shall be provided for access to this compartment.

PUMP ENCLOSURE WORK LIGHTS

Work lighting shall be provided inside the pump enclosure providing a minimum of 20 candlepower illumination.

ENGINE COMPARTMENT WORK LIGHTS

Work lighting shall be provided inside the engine enclosure that will provide a minimum of 20 candlepower illumination.

AMDOR LUMA BAR TRACK MOUNTED COMPARTMENT LIGHTS  - LED

Each individual, equipment storage compartment shall be equipped with the AMDOR Luma Bar LED light fixture mounted one each side of the forward (and rear) vertical door frame.

NFPA LIGHTING PACKAGE

The following warning light package shall include all of the minimum warning light and actuation requirements for the current revision of the NFPA 1901 Fire Apparatus Standard. The lighting as specified shall meet the requirements for both "Clearing Right of Way" and "Blocking Right of Way" as noted.

LIGHT PACKAGE ACTUATION CONTROLS

The entire warning light package shall be actuated with a single warning light switch located on the cab switch panel. The wiring for the warning light package shall engage all of the lights required for "Clearing Right of Way" mode when the vehicle parking brake is not engaged. An automatic control system shall be provided to switch the warning lights to the "Blocking Right of Way" mode when the vehicle parking brake is engaged.

UPPER LEVEL LIGHTING - WHELEN

NFPA ZONE A, UPPER

A Whelen #FN72QLED "Edge Freedom", 72" cab roof warning lightbar shall be furnished and rigidly mounted on top of the cab roof. The lightbar shall be equipped with the following:

- Two Front Corner Red Linear LED's

- Two Red Forward Facing Linear LED's

- Two White Forward Facing Linear LED's

- Two Red End Linear LED's

The forward facing clear LED flashers shall be disabled automatically for the "Blocking Right of Way" mode.

OPTICOM

The Freedom light bar shall be equipped with a #795H Low Profile LED Opticom emitter. The Opticom emitter shall be disabled automatically for the "Blocking Right of Way" mode.

ADDITIONAL LIGHTS UNITS FOR ABOVE LISTED UNIT

The Freedom light bar shall be equipped with one (1) pair(s) of #FLDRR red LED warning lights.

NFPA ZONE C, UPPER

Two (2) Whelen L31HRFN series flashing LED beacon lights shall be mounted one (1) each side at the rear of the body. A red lens shall be provided on each side.

Two (2) surface mounted Whelen 70R02FRR 700 series LED flashing light heads shall be furnished and shall be mounted one (1) each side on the upper rear face of the body, facing rear.  Each upper rear LED flashing light head shall be equipped with a red lens and chrome plated flange (7EFLANGE).

NFPA ZONES B & D REAR, UPPER

The lighting requirement for this area is covered by the lights noted in Zone "C" - Upper.

NFPA ZONES B & D FRONT, UPPER

The lighting requirement for this area is covered by the lights noted in Zone "A" - Upper.

LOWER LEVEL LIGHTING - WHELEN

NFPA ZONE A, LOWER

Two (2) Whelen #60R02FRR linear super LED light heads shall be provided and installed one (1) each side.  Each light shall be equipped with a red lens and chrome plated mounting flange.

The lower Zone A warning lights shall be mounted in the custom chassis headlight bezels.

NFPA ZONE C, LOWER

Two (2) Whelen #60R02FRR linear LED light heads shall be provided and installed one (1) each side directly below the DOT stop, tail, turn and backup lights.  Each light shall be equipped with a red lens and chrome plated mounting flange.

NFPA ZONES B & D FRONT, LOWER

Two (2) Whelen #70R02FRR linear super LED light heads shall be provided and installed one (1) each side.  Each light shall be equipped with a red lens and chrome plated mounting flange.

The lower Zone B & D warning lights shall be mounted on the sides of the custom chassis front bumper.

NFPA ZONES B & D MIDSHIP, LOWER

Two (2) Whelen #70R02FRR linear super LED light heads shall be provided and installed one (1) each side.  Each light shall be equipped with a red lens and chrome plated mounting flange.

NFPA ZONES B & D REAR, LOWER

Two (2) Whelen #70R02FRR super LED light heads shall be provided and installed one (1) each side.  Each light shall be equipped with a red lens and chrome plated mounting flange.

WARNING LIGHT SYSTEM CERTIFICATION

The warning light system(s) specified above shall not exceed a combined total amperage draw of 45 AMPS with all lights activated in either the "Clearing Right of Way" or the "Blocking Right of Way" mode.

The warning light system(s) shall be certified by the light system manufacturer(s), to meet all of the requirements in the current revision of the NFPA 1901 Fire Apparatus Standard as noted in the General Requirements section of these specifications. The NFPA required "Certificate of Compliance" shall be provided with the completed apparatus.

ROOF MOUNTED LIGHT BARS

A pair of Whelen Model FNMINI, 24" Freedom, cab roof warning light bars shall be furnished and rigidly mounted, one (1) at each side on the cab roof facing to each side of the unit. Each light bar shall be equipped with two (2) red corner LED's, one (1) forward facing LED and one (1) side facing LED. All the lenses shall be clear.

The lights specified above shall be provided in addition to the NFPA required Optical Warning Light Package and shall be switched independently from the light package. Additionally, wiring for the independently switched lights specified, shall be run through the Load Management System to ensure that the electrical system is not overloaded by the additional amperage draw requirements.

TRAFFIC ADVISER WARNING LIGHT

One (1) Whelen LED "Traffic Advisor", Model TAL85 48", rear directional light shall be installed on the rear of the body. The light shall be equipped with eight (8) lamps. The directional light shall be activated by a control module. The control module shall be conveniently located near the driver's position. The rear directional light shall be wired through the load management system of the unit.

ELECTRIC HORN

A single electric horn activated by the steering wheel horn button shall be furnished.

BACK-UP ALARM

A Preco, Model #250, solid state backup alarm shall be provided and installed at the rear of the apparatus under the tailboard. The backup alarm shall activate automatically when the transmission is placed in reverse gear and the ignition is "on".

AIR HORNS

Two (2) chrome plated air horns shall be at the front of the vehicle. The air horns shall be mounted in full compliance with NFPA-1901. A 3/8" minimum air line "teed" with equal distance from each horn shall be installed.

Both air horns shall be recessed in the front bumper.

The air horn(s) shall be controlled by a push button located on the dash, on the officer's side and the steering horn button for the driver. An air horn/standard horn selector switch shall be furnished on the dash for the drivers steering horn button.

AIR HORN SHUT-OFF VALVE

A shut-off valve shall be provided for the air horn supply line.

ELECTRONIC SIREN

One (1) Whelen #295SLSA1, 200 watt electronic siren shall be provided featuring: bottom mount control head in cab, "Si-Test" self diagnostic feature, six (6) function siren, radio repeat and public address.

The electronic siren and speaker shall meet the NFPA required SAE certification to ensure compatibility between the siren and speaker.

SIREN SPEAKER

One (1) Federal, Model #ES100 siren speaker shall be provided, recessed in the front bumper and wired to the electronic siren.

FEDERAL Q2B MECHANICAL SIREN

One (1) Federal Model #Q2B mechanical siren shall be provided to provide audible warning.

The Q2B siren shall be wired through the load management system to prevent excessive amperage draw. The siren shall be provided in addition to the required minimum NFPA audible warning requirements.

The Q2-B siren shall be semi-recessed into the bumper on the officer's side. The siren shall be recessed so the front grille portion of the siren is exposed and protruding beyond the bumper.

Two (2) Linemaster #632 floor mounted foot switches shall be provided, one (1) for the officer and one (1) for the driver. A siren brake button shall be provided near the driver's position.

FIRECOM MODEL #3010 INTERCOM SYSTEM

A Firecom Model #3010 intercom system shall be provided in the front of the cab. The system shall be capable of interfacing with a two-way radio system (note: an authorized two-way radio installer shall be responsible for interfacing the intercom system with the two-way radio). The master station shall be capable of accepting up to six positions (plus exterior positions), and utilize a 12 volt nominal power supply. The unit shall have a touch screen adjustable volume control and have advanced noise reducing circuitry. The unit shall also be housed in a rugged steel casing, which shall be mounted on the engine enclosure.

The intercom system shall include:

DRIVERS AND OFFICERS HEADSETS FOR FIRECOM SYSTEM

Two (2) UH-10 single-plug under helmet radio transmit headsets shall be furnished for the driver and officer seating locations in the cab. The headsets shall have adjustable volume, noise-canceling electric microphone, adjustable head strap, and a flex-style boom which rotates for left or right dress. The sets shall also have comfortable liquid foam ear seals.

Two (2) HM-10 plug in modules shall be furnished at the drivers and officers locations in the forward area of the cab.

REAR JUMPSEAT HEADSETS

Four (4) UH-20 single-plug under helmet intercom headsets shall be furnished for four (4) rear jump seat locations. The intercom headsets shall have adjustable volume, noise-canceling electric microphone, adjustable head strap, and a flex-style boom which rotates for left or right dress. The sets shall also have comfortable liquid foam ear seals.

Four (4) HM-10 plug in modules shall be furnished in the rear crew area of the cab at the jump seat locations to accommodate the intercom headsets.

Two (2) rubber coated steel headset hanger hooks shall be furnished in the front section of the cab to hold the driver and officer intercom headsets while not in use.

Four (4) rubber coated steel headset hanger hooks shall be furnished to hold the crew intercom headsets while not in use.

EXTERNAL PLUG-IN

One (1) PP-20 water resistant plug-in modules shall be furnished for intercom headset acceptance at the pump panel.

RADIO INTERFACE CABLE

One (1) radio interface cable, Model #110-5101-30-20 shall be provided and installed from the firecom base unit to the area of where the mobile radio base station shall be mounted. The end of the cable that connects to the mobile radio shall be un-terminated and shall be the responsibility of the radio installer to provide and install the correct adapter to connect the cable to the mobile radio.

PUMP

- WATEROUS CSU-C20

- 1500 G.P.M.

- SINGLE-STAGE

The pump shall be of single-stage construction and shall comply with all applicable requirements of the latest standards for automotive fire apparatus of the National Fire Protection Association, NFPA-1901 and shall have a rated capacity of 1500 gpm.

The pump must deliver the percentage of rated capacity at the pressure listed below:

- 100% of rated capacity at 150 P.S.I. net pump pressure

- 100% of rated capacity at 165 P.S.I. net pump pressure

- 70% of rated capacity at 200 P.S.I. net pump pressure

- 50% of rated capacity at 250 P.S.I. net pump pressure

When dry, the pump shall be capable of taking suction and discharge water with a lift of 10 feet in not more than 30 seconds through 20 feet of appropriate size suction hose.

The pump shall be free from objectionable pulsation and vibration under all normal operating conditions.

PUMP CONSTRUCTION

The pump body shall be close-grained gray iron and must be horizontally split in two sections for easy removal of the impeller shaft assembly, and designed for complete servicing from the bottom of the truck without disturbing setting of the pump in the chassis or apparatus piping which is connected to the pump. Pump body halves shall be bolted together on a single horizontal face to minimize chance of leakage and facilitate reassemble.

Discharge manifold shall be cast as an integral part of the pump body assembly and shall provide at least three full 3-1/2 inch openings for ultimate flexibility in providing various discharge outlets for maximum efficiency, and shall be located as follows: one outlet on the right side of the pump body, one outlet on the left side of the pump body, and one outlet on top of the pump discharge manifold.

IMPELLER SHAFT

The impeller shaft shall be stainless steel, accurately ground to size, and supported at each end by oil or grease lubricated, anti-friction bearings for rigid and precise support. Bearings shall be protected from water and sediment by suitable stuffing boxes, flinger rings and oil seals. The impeller shaft shall be of two-piece construction separable between the pump and pump transmission to allow true separation of the transmission from the pump without disassembly of either component. No sleeve type bearings shall be used.

PUMP PACKING

Stuffing boxes shall be equipped with two-piece glands to permit adjustment or replacement of packing without disturbing the pump. Lantern rings shall be located at the inner end of the stuffing boxes the all ring can be removed without removal of the lantern rings. Water shall be fed into the stuffing box lantern rings for proper lubrication and cooling when the pump is operating.

PUMP IMPELLER

The impeller shall be bronze, accurately balanced (mechanically and hydraulically), of mixed flow design with reverse flow labyrinth-type wear rings that resist water bypass and loss of efficiency due to wear.

Wear rings shall be bronze, and shall be easily replaceable to restore original pump efficiency and eliminate the need for replacing the entire pump casing due to wear.

PUMP TRANSMISSION

The pump transmission shall be an all aluminum "C20" Model, rigidly attached to the pump body assembly and be of latest design incorporating a high strength involute tooth-form Hy-Vo chain drive. The driven sprockets shall be capable of operating at high speeds to provide smooth, quiet transfer of power. The shift engagement shall be accomplished by a free-sliding collar and shall incorporate an internal locking mechanism to insure that the collar shall be maintained in ROAD or PUMP position.

PUMP RATIO

The pump ratio shall be selected by the apparatus manufacturer to give maximum performance with the engine and transmission selected.

The manufacturer shall supply at time of delivery copies of the pump manufacturer's certification of hydrostatic testing, the engine manufacturer's current certified brake horsepower curve.

PUMP SHIFT CONTROL

The drive unit shall be equipped with a power shift. The shifting mechanism shall be a heat treated, hard anodized aluminum power cylinder with stainless steel shaft.

The pump shift control, pump engaged light and ok to pump indicator light shall be provided utilizing the International multi-plex system. They shall be located in the lower left switch panel.  Switch to be YELLOW in color with a three sided guard around it to denote being for a strategic type switch function. A standard International air solenoid pack shall be utilized to lock the transfer case in road or pump.

This control shall be electronically interlocked through the International multi-plex system to prevent inadvertent activation or de-activation. This allows the control to be interlocked with engine rpm, transmission gear status and park brake state. The switch positions and indicator lights shall be clearly marked. The pump shift switch shall also serve as the manual lock up switch; in case of air pressure lose. An air operated in-cab control for rapid shift shall be provided that locks in road or pump, with a neutral position for use when manual override is required.

EMERGENCY PUMP SHIFT

An emergency manual pump shift control shall be furnished on the left side pump panel which may be utilized if the air shift control does not operate.

TRANSMISSION LOCK

The automatic transmission furnished in the chassis shall have a lock-up assembly which brings the transmission to direct drive and prevents the transmission from shifting gears while in the pumping mode.

BRAKING SYSTEM

A positive braking system shall be provided to prevent vehicle movement during pumping operations. The air brakes furnished must satisfy this requirement.

PUMP MOUNTS

Extra heavy duty pump mounting brackets shall be furnished. These shall be bolted to the frame rails in such a position to perfectly align the pump so that the angular velocity of the drive line joints shall be the same on each end of the drive shaft. This shall assure full capacity performance with a minimum of vibration. Mounting hardware shall utilize Grade 8 bolts.

Pumps which are not mounted directly to the frame will not be considered. Under no circumstance shall the pump function as a frame cross member.

PRESSURE RELIEF VALVE

A Waterous relief valve system shall be positive and quick acting, and shall have a control valve to provide instantaneous hydraulic lock-out which does not require the operator to cancel out or disturb the pressure setting. Relief valve control (pilot valve) shall be protected from malfunction due to sand or other sediment in the water by a strainer which can be removed, cleaned and replaced from the operator's panel while the pump is operating. Relief valve indicator lights shall be provided and mounted on the panel adjacent to the pilot valve assembly. The indicator lights are to be "amber" and marked OPEN to indicate the relief valve is bypassing and "green" marked CLOSED to indicate when the relief valve is closed.

PUMP PRESSURE CONTROL SYSTEM

The apparatus shall be equipped with a Fire Research PumpBoss Model# PBA400 pressure governor and monitoring display kit.  The kit shall include a control module, intake pressure sensor, discharge pressure sensor, and cables. The control module case shall be waterproof and have dimensions not to exceed 6 3/4" high by 4 5/8" wide by 1 1/2" deep. The control knob shall be 2" in diameter with no mechanical stops, have a serrated grip, and a red idle push button in the center. It shall not extend more than 1 3/4" from the front of the control module. Inputs for monitored information shall be from a J1939 databus or independent sensors. Outputs for engine control shall be on the J1939 databus or engine specific wiring. Inputs to the control module from the pump discharge and intake pressure sensors shall be electrical.

The following continuous displays shall be provided:

Engine RPM; shown with four daylight bright LED digits more than 1/2" high

Check engine and stop engine warning LEDs

Oil pressure; shown on a dual color (green/red) LED bar graph display

Engine coolant temperature; shown on a dual color (green/red) LED bar graph display

Transmission Temperature: shown on a dual color (green/red) LED bar graph display

Battery voltage; shown on a dual color (green/red) LED bar graph display

Pressure and RPM operating mode LEDs

Pressure / RPM setting; shown on a dot matrix message display

Throttle ready LED.

The dot-matrix message display shall show diagnostic and warning messages as they occur. It shall show monitored apparatus information, stored data, and program options when selected by the operator. All LED intensity shall be automatically adjusted for day and night time operation.

The program shall store the accumulated operating hours for the pump and engine to be displayed with the push of a button. It shall monitor inputs and support audible and visual warning alarms for the following conditions:

High Battery Voltage

Low Battery Voltage (Engine Off)

Low Battery Voltage (Engine Running)

High Transmission Temperature

Low Engine Oil Pressure

High Engine Coolant Temperature

Out of Water (visual alarm only)

No Engine Response (visual alarm only).

The program features shall be accessed via push buttons located on the front of the control module. There shall be a USB port located at the rear of the control module to upload future firmware enhancements.

The governor shall operate in two control modes, pressure and RPM. No discharge pressure or engine RPM variation shall occur when switching between modes. A throttle ready LED shall light when the interlock signal is recognized. The governor shall start in pressure mode and set the engine RPM to idle. In pressure mode the governor shall automatically regulate the discharge pressure at the level set by the operator. In RPM mode the governor shall maintain the engine RPM at the level set by the operator except in the event of a discharge pressure increase. The governor shall limit a discharge pressure increase in RPM mode to a maximum of 30 psi. Other safety features shall include recognition of no water conditions with an automatic programmed response and a push button to return the engine to idle.

The pressure governor and monitoring pressure display shall be programmed to interface with a specific engine.

AKRON INTAKE RELIEF VALVE

An Akron Model 59 intake relief valve system shall be plumbed on the suction side of the pump to comply fully with NFPA-1901 requirements. Excess pressures shall be plumbed to discharge water under the pump enclosure away from the pump operator.

PUMP CERTIFICATION

The pump shall be third party performance tested to meet the requirements of NFPA-1901.  To ensure top quality and integrity, the test company shall be Underwriter's Laboratories (UL). NO EXCEPTIONS!

PRIMING PUMP

The priming pump shall be a 12-volt Waterous Model VPO Oil-Less, positive displacement vane type, electrically driven. One priming control shall open the priming valve and start the priming motor. The primer shall be capable of priming without the use of primer oil. The primer shall be connected to the power source with a 300 amp fusible link.

PRIMING VALVE

The primer shall be activated by an automatic electrical/mechanical valve with a single push button control located on the pump operator's panel. Valve actuation may be accomplished while the main pump is operational, if necessary to assure complete prime. A control arm on the priming valve shall allow manual override if electrical failure occurs. The primer shall be connected to the power source with a 300 amp fusible link.

MASTER DRAIN

The Waterous manifold drain assembly shall consist of a stainless steel plunger in a bronze body with multiple ports. The valve shall be designed so that pump discharge pressure prevents it from opening accidentally. The drain valve control shall be panel mounted, cable or rod operated and identified PUMP DRAIN.

INDIVIDUAL BLEEDERS AND DRAINS

All lines shall drain through the master drain valve or shall be equipped with individual drain valves, easily accessible and labeled.

One (1) individual "CLASS ONE" quarter turn drain valve shall be furnished for each  1-1/2" or larger discharge port and each 2-1/2" gated auxiliary suction.

Drain/bleeder valves shall be located at the bottom of the side pump module panels.

All drains and bleeders shall discharge below the running boards.

SYNFLEX SUCTION, DISCHARGE, PRESSURE AND CONTROL LINES

Small lines within the pump enclosure shall be constructed from Synflex hose. Uses include, but are not limited to such lines as priming control, gauge lines, drain lines, air control valves, pump shift, supplemental cooling, foam flush and air bleeder valves.

ANODE BLOCKS

Two (2) Waterous zinc anode blocks shall be provided and located on the suction side of the pump to protect the pump from corrosion.

The Anodes shall be painted Safety Yellow for identification purposes.

PUMP MODULE

The pump module shall be a self-supported structure mounted independently from the body and chassis cab. The design must allow normal frame deflection without imposing stress on the pump module structure or side running boards. The pump module shall be securely mounted to the chassis frame rails.

The pump module shall be a welded frame work utilizing structural stainless steel components properly braced to withstand the rigors of chassis frame flex.

DUNNAGE AREA

A dunnage area shall be provided above the pump enclosure for equipment mounting and storage. This area shall be furnished with a removable 3/16" aluminum tread plate floor and side panels.

NOTE: The size of this storage area may vary when top mounted crosslays, booster reel(s), etc., are specified and located in this area.

SUCTION INLETS

Two (2) 6" N.S.T. suction inlets shall be provided, one on the driver side pump panel and one on the officer side pump panel. A removable strainer shall be installed on each inlet.

PUMP SUCTION ENDS

The main pump suction inlets shall be furnished with a short suction end, terminating with only the suction threads protruding through the side panel to minimize the distance an exterior appliance protrudes beyond the pump panel.

One (1) 6" NST chrome plated long handle pressure vented cap shall be installed on each.

FRONT SUCTION

A 6" N.S.T. front suction inlet shall be provided at the front of the vehicle, plumbed from the pump.

The front inlet shall be located above the right hand side of the front bumper extension and shall terminate with a chromed brass, chicksan style swivel to allow a minimum of 180 degree rotation of the inlet for suction hose attachment.

The front suction pipe shall be equipped with a chrome 6" NSTM thread adapter.

The front inlet shall be plumbed utilizing 5", schedule 10 stainless steel piping, 45 degree weld elbows and a limited number of 90 degree sweep elbows in a welded assembly from the pump to the front of the cab.

A minimum of two (2) grooved pipe couplings shall be furnished in this assembly to allow for flex and serviceability.

BUTTERFLY VALVE

The front suction inlet shall be gated with a 5" Bray in-line, full flow butterfly valve, located in the pump compartment.

An Akron Model 59 inlet relief valve shall be provided as part of the front suction plumbing, situated outboard of the rear suction gate valve.

The front suction valve shall be air operated with a control switch located on the operator's panel with function plate.

FRONT INLET SWIVEL

One (1) 6" NST chrome plated long handle vented cap(s) shall be installed on front suction.

AUXILIARY SIDE SUCTION(S)

AUXILIARY INLET – DRIVERS SIDE

One (1) 2-1/2" auxiliary suction shall be provided at the driver side pump panel, to the rear of the main inlet. The 2-1/2" auxiliary suction shall terminate with a removable strainer, chrome plated 2-1/2" NST female swivel with a chrome plated plug and retaining chain.

A 2 1/2" Akron #8800 series full flow, stainless steel ball valve shall be provided for the driver side rear auxiliary suction.

A 1/4 turn push/pull control handle shall be provided on the driver side rear auxiliary suction valve

AUXILIARY INLET – OFFICER SIDE

One (1) 2-1/2" auxiliary suction shall be provided at the officer side pump panel, to the front of the main inlet. The 2-1/2" auxiliary suction shall terminate with a removable strainer, chrome plated 2-1/2" NST female swivel with a chrome plated plug and retaining chain.

A 2 1/2" Akron #8800 series full flow, stainless steel ball valve shall be provided for the officer side front auxiliary suction.

A 1/4 turn push/pull control handle shall be provided on the officer side rear auxiliary suction valve

All side gated inlet valves shall be recess mounted behind the side pump panels or body panels. (No Exceptions)

TANK TO PUMP

One (1) 3" tank to pump line shall be, piped through the front bulkhead of the tank with a 90 degree elbow down into the tank sump. This line shall be plumbed directly into the rear of the pump suction manifold for maximum efficiency.

A check valve shall be provided to prevent accidental pressurization of the water tank through the pump connection. Connection from the valve to the tank shall be made by using a non-collapsible flexible rubber hose.

A 3" Akron #8800 series full flow, stainless steel ball valve shall be provided between the pump suction manifold and the water tank.

A push/pull control handle shall be located on the operator's panel with function plate.

TANK FILL

One (1) 2" gated full flow pump to tank refill line controlled at the pump panel shall be provided. A deflector shield inside the tank shall be furnished. Tank fill plumbing shall utilize 2" high pressure hose for tank connection to accommodate flexing between components. (NO EXCEPTIONS)

A 2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided between the pump discharge manifold and the water tank.

A push/pull control handle shall be located on the operator's panel with function plate.

DRIVER'S SIDE MAIN DISCHARGE #1

A discharge shall be provided and located at the driver's side pump panel. The driver's side discharges #1 shall terminate with NST threads, through the left panel above the main pump intake.

The main pump discharge shall be plumbed directly from the pump discharge manifold utilizing direct connect discharge valve flanges.

A 2 1/2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the driver's side #1 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The discharge valve shall be equipped with a straight 2 1/2" NST adapter that shall be equipped with a 2 1/2" NST, 30-degree, chrome plated elbow.

A 2 1/2" NST chrome plated pressure vented cap shall be installed on driver's side #1 discharge.

The driver's side #1 discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The driver's side #1 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

DRIVER'S SIDE MAIN DISCHARGE #2

A discharge shall be provided and located at the driver's side pump panel. The driver's side discharges #2 shall terminate with NST threads, through the left panel above the main pump intake.

The main pump discharge shall be plumbed directly from the pump discharge manifold utilizing direct connect discharge valve flanges.

A 2 1/2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the driver's side #2 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The discharge valve shall be equipped with a straight 2 1/2" NST adapter that shall be equipped with a 2 1/2" NST, 30-degree, chrome plated elbow.

A 2 1/2" NST chrome plated pressure vented cap shall be installed on driver's side #2 discharge.

The driver's side #2 discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The driver's side #2 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

OFFICER'S SIDE MAIN DISCHARGE #1

A discharge shall be provided and located at the officer's side pump panel. The officer's side discharges #1 shall terminate with NST threads, through the officer's side panel above the main pump intake.

The main pump discharge shall be plumbed directly from the pump discharge manifold utilizing direct connect discharge valve flanges.

A 2 1/2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the officer's side #1 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The discharge valve shall be equipped with a straight 2 1/2" NST adapter that shall be equipped with a 2 1/2" NST, 30-degree, chrome plated elbow.

A 2 1/2" NST chrome plated pressure vented cap shall be installed on officer's side #1 discharge.

The officer's side #1 discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The officer's side #1 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

OFFICER'S SIDE MAIN DISCHARGE #2

A discharge shall be provided and located at the officer's side pump panel. The officer's side discharges #2 shall terminate with NST threads, through the officer's side panel above the main pump intake.

The main pump discharge shall be plumbed directly from the pump discharge manifold utilizing direct connect discharge valve flanges.

A 4" Akron, #8840 series, full flow, flat ball valve shall be provided for the officer's side #2 discharge.

The discharge valve shall be equipped with a straight 4" NST adapter that shall be equipped with a 4" NST, 30-degree, chrome plated elbow.

The officer's side #2 discharge cap provided as standard equipment shall be deleted.

A 4" NSTF X 5" Storz Kochek S37S straight adapter w/cap shall be provided on the officer's side #2 discharge.

The officer's side #2 discharge valve shall be equipped with an Akron Brass Style 9313 Valve Controller. The electric controls must be of current limiting design, requiring no clutches in the motor. The unit must have booted switches with momentary open and close as well as an optional one touch full open feature to operate the actuator.  The unit must provide position indication through 10 LED light indicators for maximum visibility.

The officer's side #2 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

OFFICER'S SIDE MAIN DISCHARGE #3

A discharge shall be provided and located at the officer's side pump panel.  The officer's side discharges #3 shall terminate with NST threads, through the officer's side panel above the main pump intake.

The main pump discharge shall be plumbed directly from the pump discharge manifold utilizing direct connect discharge valve flanges.

A 2 1/2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the officer's side #3 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The discharge valve shall be equipped with a straight 2 1/2" NST adapter that shall be equipped with a 2 1/2" NST, 30-degree, chrome plated elbow.

A 2 1/2" NST chrome plated pressure vented cap shall be installed on officer's side #3 discharge.

The officer's side #3 discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The officer's side #3 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

DRIVER SIDE HOSE BED DISCHARGE

A 1 1/2" rear hose bed discharge shall be plumbed to the upper front body panel, extending into the front of the hose bed.

The rear hose bed discharge shall terminate at the top of the body panel, in the driver side front of the hose bed.

The driver side hose bed discharge pipe shall be equipped with a chrome 1 1/2" NSTM thread adapter.

The driver side hose bed discharge shall be plumbed utilizing 2" schedule 10, stainless steel piping, 45 degree threaded elbows and a limited number of 90 degree sweep elbows in an  assembly from the pump to the rear of the vehicle.

A minimum of one (1) grooved pipe coupling shall be furnished in this assembly to allow for flex and serviceability.

A 2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the driver side hose bed discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The driver’s side hose bed discharge valve shall be controlled by a push/pull handle located on the operator's panel.

One (1) 1 1/2" NST chrome plated pressure vented cap(s) shall be installed the driver's side hose bed discharge.

The driver's side hose bed discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

OFFICER'S SIDE

A 2 1/2" NST rear hose bed discharge shall be plumbed to the upper front body panel, extending into the front of the hose bed.

The rear hose bed discharge shall terminate at the top of the body panel, in the right front of the hose bed.

The officer's side hose bed discharge pipe shall be equipped with a chrome 2 1/2" NSTM thread adapter.

The officer's side hose bed discharge shall be plumbed utilizing 2 1/2" schedule 10, stainless steel piping, 45 degree threaded elbows and a limited number of 90 degree sweep elbows in an assembly from the pump to the rear of the vehicle.

A minimum of one (1) grooved pipe coupling shall be furnished in this assembly to allow for flex and serviceability.

A 2 1/2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the hose bed officer's side rear discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The officer's side hose bed discharge valve shall be controlled by a push/pull handle located on the operator's panel.

One (1) 2 1/2" NST chrome plated pressure vented cap(s) shall be installed the officer's side hose bed discharge.

The officer's side hose bed discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

DECK GUN DISCHARGE

A deck gun discharge shall be plumbed from the pump to an area on top of the vehicle. The deck gun piping shall be firmly supported and braced.

The deck gun discharge shall be located in the center of the dunnage area above the pump module. A pedestal type, 1/4" steel plate support assembly shall be provided to stabilize deck gun plumbing below deck gun mount flange.

The deck gun discharge pipe shall terminate with 3" NPT threads.

To improve the operation range of the deck gun, the discharge pipe shall be outfitted with a TFT (18") Extend-A-Gun, part # XG18VL-PL. The Extend-A-Gun shall be wired to the hazard light on the cab dash.

The deck gun piping shall be designed so the overall height of the deck gun in the mounted/stowed position does not exceed the tallest point on the cab/body.

The deck gun discharge shall be plumbed utilizing 3" schedule 10, stainless steel piping, 45 degree threaded elbows and a limited number of 90 degree sweep elbows in an assembly from the pump to the deck gun location.

A minimum of one (1) grooved pipe coupling shall be furnished in this assembly to allow for flex and serviceability.

A 3" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the deck gun discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The deck gun discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The deck gun discharge shall be equipped with a 2 ½" diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

FRONT DISCHARGE

A 1 1/2" front #1 discharge shall be plumbed to the front bumper of the vehicle.

The front #1 discharge shall terminate on the top driver's side of the front bumper extension gravel shield with a chrome 1 1/2" NST chicksan swivel adapter.

The front #1 discharge shall be plumbed utilizing 2" schedule 10, stainless steel piping, 45 degree threaded elbows and a limited number of 90 degree sweep elbows in an assembly from the pump to the front of the vehicle.

A minimum of one (1) grooved pipe coupling shall be furnished in this assembly to allow for flex and serviceability. Automatic discharge drains shall be provided at all low points in the plumbing.

A 2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the front  #1 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The front #1 discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The front #1 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

HORIZONTAL CROSSLAY #1

A crosslay hose bed shall be provided and plumbed from the pump in a transverse design, located above the pump enclosure for quick attack deployment. The crosslay hose bed flooring shall be designed to be removable, constructed from brushed finish, perforated aluminum material.

Crosslay #1 shall be designed to have a minimum total capacity of 3.5 cubic feet as required by NFPA -1901 to accommodate a minimum of 200 feet of 1-3/4" fire hose.

Crosslay #1 hosebed shall be designed to accommodate the fire hose in a double stack configuration.

The crosslay discharge shall terminate below the hosebed floor with a 1 1/2" NSTM chicksan swivel adapter. The crosslay hose bed floor shall be slotted to allow the swivel to extend up through the floor, allowing the pre-connected hose to be pulled off either side of the apparatus without kinking the hose at the coupling connection.

The crosslay #1 discharge shall be plumbed utilizing 2" schedule 10, stainless steel piping and/or flexible hose, 45 degree threaded elbows and a limited number of 90 degree sweep elbows in an assembly from the pump to crosslay hosebed.

A minimum of one (1) grooved pipe coupling shall be furnished in this assembly to allow for flex and serviceability.

A 2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the crosslay #1 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The crosslay #1 discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The crosslay #1 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

HORIZONTAL CROSSLAY #2

A crosslay hose bed shall be provided and plumbed from the pump in a transverse design, located above the pump enclosure for quick attack deployment. The crosslay hose bed flooring shall be designed to be removable, constructed from brushed finish, perforated aluminum material.

Crosslay #2 shall be designed to have a minimum total capacity of 3.5 cubic feet as required by NFPA -1901 to accommodate a minimum of 200 feet of 1-3/4" fire hose.

Crosslay #2 hosebed shall be designed to accommodate the fire hose in a double stack configuration.

The crosslay discharge shall terminate below the hosebed floor with a 1 1/2" NSTM chicksan swivel adapter. The crosslay hose bed floor shall be slotted to allow the swivel to extend up through the floor, allowing the pre-connected hose to be pulled off either side of the apparatus without kinking the hose at the coupling connection.

The crosslay #2 discharge shall be plumbed utilizing 2" schedule 10, stainless steel piping and/or flexible hose, 45 degree threaded elbows and a limited number of 90 degree sweep elbows in an assembly from the pump to crosslay hosebed.

A minimum of one (1) grooved pipe coupling shall be furnished in this assembly to allow for flex and serviceability.

A 2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the crosslay #2 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The crosslay #2 discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The crosslay #2 discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

CROSSLAY HEIGHT FROM GROUND LEVEL

The crosslay hose bed floor will be approximately 42" above the side running board and no more than 66" above ground level.

PUMP ENCLOSURE HOSEBED HOSE RETENTION

A vinyl cross lay cover shall be provided. It shall be securely fastened at the front with snaps and Velcro at the rear, with straps to secure each end flap.

The crosslay cover shall be red in color.

BOOSTER REEL #1 DISCHARGE

A 1 1/2" booster reel discharge shall be plumbed from the pump to the booster reel.

The booster reel discharge shall be plumbed from the valve to the hose reel utilizing 1" high pressure hose. The end of the hose connected to the hose reel shall be equipped with a swivel end for ease in hose replacement.

A 1 1/2" Akron, #8800 series, full flow, stainless steel ball valve shall be provided for the booster reel #1 discharge. The valve shall be equipped with the Akron "Tork-Lok" feature.

The booster reel discharge valve shall be controlled by a push/pull handle located on the operator's panel.

The booster reel discharge shall be equipped with a 2 ½ “ diameter Noshok pressure gauge. The gauge shall have a rugged corrosion free stainless steel case and clear scratch resistant molded crystals with captive O-ring seals to ensure distortion free viewing and seal the gauge. The gauge shall be filled with a synthetic mixture to dampen shock and vibration, lubricate the internal mechanisms, prevent lens condensation and ensure proper operation from –40°F to +160°F.

The gauge shall exceed ANSI B40.1 Grade A requirements with an accuracy of +/- 1.5% full scale and include a size appropriate phosphorous bronze bourdon tube with a reinforced lap joint and large tube base to increase the tube life and gauge accuracy.

A polished chrome-plated stainless steel bezel shall be provided to prevent corrosion and protect the lens and gauge case. The gauge shall have black graphics on a white background.

BOOSTER REEL #1

One (1) Hannay, aluminum, Super Booster, electric rewind booster reel shall be furnished.  The reel shall be equipped with a water lubricated; self flushing, bronze swivel joint and an adjustable brake for free wheeling, drag or full lock operation.

The booster reel #1 shall be mounted above the pump enclosure towards the officer side of the unit.

Booster reel rewind shall be controlled by a pump panel mounted push button on the officer's side panel. The booster reel circuit shall be equipped with a shielded toggle switch to act as a booster reel disconnect to avoid accidental actuation of the booster reel rewind button.

Each booster reel shall be equipped with 150' of 1" booster hose in (1) 100' section and (1) 50' section. Each length shall be fitted with NST couplings.

Two (2) horizontal hose rollers of polished stainless steel and guide spools shall be placed one (1) on each side panel.

One (1) booster reel air blowout utilizing a quarter turn shuttle valve to redirect chassis air to the booster reel shall be provided at the pump operator's panel for cold weather operations.

FOAM PIPING

All foam concentrate plumbing from the tank or auxiliary foam inlet to the foam system components shall be stainless steel.

The foam system piping shall incorporate a check valve to prevent water from entering the foam tank; the discharge piping shall also include a check valve to prevent foam solution from back feeding into the discharge side of the pump. Individual discharge piping shall be as specified for each discharge.

The complete foam system shall be tested in accordance with Chapter 17 of NFPA-1901.

FOAM SYSTEM (SINGLE DISCHARGE)

An Akron #3096, in-line, bypass foam system shall be provided, which incorporates an operator's panel controlled in-line foam eductor plumbed into the specified 1 1/2" discharge to flow foam at a maximum rate of 95 gallons per minute. The eductor shall be capable of bypassing the foam venturi to allow higher GPM flows through the discharge. This system shall include an operator's panel mounted metering valve and individual controls for the foam eductor and foam flush.

The in-line foam system shall be installed in the crosslay #1 discharge plumbing.

PUMP PANEL - SIDE MOUNT

The pump operator's control panel shall be located on the driver side of the apparatus. The pump enclosure side panels shall be completely removable and designed for easy access and servicing.

PUMP PANEL MATERIAL

The left side operator's panel, gauge panel, right side pump panel and right side access door shall be fabricated from 1/8" aluminum, coated with black Speedliner material. The Speedliner material shall provide a non-glare, rubberized textured finish.

HINGED GAUGE PANEL

A full width, vertically hinged gauge access panel shall be provided at the operator's position. Chrome plated positive locks shall be provided along with chain holders to prevent the front of the gauge panel from coming in contact with other panels when open.

HINGED PUMP ACCESS DOOR

An 18" high by a minimum of 30" wide pump enclosure access door shall be provided above the officer's side pump panel. This door shall have a "D" ring, two-point latch mechanism and two (2) gas shock stay arms for ease of access.

PUMP ACCESS PANELS

Two (2) removable pump access panels shall be furnished at the forward area of the pump enclosure accessed from the front when the cab is tilted. Each access panel shall be fabricated from 1/8" aluminum tread plate.

PANEL FASTENERS

Stainless steel machine screws and lock washers shall be used to hold these panels in position. The panels shall be easily removable to provide complete access to the pump for major service.

CAPS AND ADAPTERS SAFETY TETHER

All applicable discharge and suction caps, plugs and adapters shall be equipped with chrome plated ball chain or double looped coil chain and secured to the vehicle.

PUMP PANEL TRIM PLATES

A high polish stainless steel trim plate shall be provided around each discharge port and suction inlet opening to allow accessibility to the respective valve for service and repairs.

DISCHARGE GAUGE TRIM BEZELS

Each individual discharge gauge shall be installed into a decorative chrome-plated mounting bezel that incorporates valve-identifying verbiage and color labels.

COLOR CODED IDENTIFICATION TAGS

Color coded identification tags shall be provided for all gauges, controls, connections, switches, inlets and outlets.

PUMP OPERATOR'S PANEL LIGHT SHIELD

The pump operator’s panel shall be equipped with a light shield that shall be full width of the control panel, and shall be positioned to cover the lights and prevent glare.

The light shield shall be equipped with the following lights:

- Four (4) Weldon #2631 LED lights

One (1) light under the operator's panel light shield shall be actuated when fire pump is engaged in addition to the pump engaged light.

OFFICER SIDE  PANEL LIGHT SHIELD

The officer side pump panel shall be equipped with a light shield that shall be full width of the control panel, and shall be positioned to cover the lights and prevent glare.

The light shield shall be equipped with the following lights:

- Four (4) Weldon #2631 LED lights

The lights shall be switched with the operator panel lights.

PUMP OPERATOR'S PANEL

Particular attention is to be given to functional arrangement of all controls. The pump operator's panel shall accommodate the following:

- Hinged gauge panel

- Water tank fill valve

- Auxiliary suction valve control

- All discharge valve controls

- Auxiliary engine cooler controls

- Water tank suction control valve

- Pump primer valve

- Engine throttle control

- Master compound vacuum gauge

- Master pressure gauge

- Individual discharge gauges

- Pump shift engaged indicator light

- Water tank water level indicator

- Engine tachometer

- Engine oil pressure gauge with audible alarm

- Engine water temperature gauge with audible alarm

- Low voltage light and audible alarm

- Pump panel light switch

- Speed counter (Underwriters)

- Pump performance plate (Underwriters)

- Pump serial No. plate

- Master pump drain valve

- Individual drains

- Voltmeter

- Air inlet/outlet at lower left hand panel

- Relief valve with indicator light

- Relief valve drains

- Fuel Gauge

- Pump panel air horn actuation button

- Air inlet/outlet chuck (right side panel)

- Fire Research "Pump Boss" pressure governor control

- Waterous pressure relief valve control

PUMP TEST PORTS

The pump panel shall be equipped with Vacuum & Pressure test plugs to allow for test equipment to monitor pump pressure and vacuum levels. Chrome plugs and labels shall be provided for the test ports.

MASTER GAUGES

One (1) 4" diameter pressure gauge (labeled: "PRESSURE") and one (1) 4" diameter compound vacuum gauge (labeled: "INTAKE") shall be provided. The master gauges shall be "No Shok", silicone filled. The gauge faces shall be white with black numerals.

PRESSURE & COMPOUND GAUGE RANGES

All applicable pressure gauges shall have a range of 0 - 400 P.S.I., and the compound gauge shall have a range of -30" - 0 - 400 P.S.I.

ENGINE COOLER

An auxiliary cooler or heat exchanger shall be installed in the engine compartment between the engine and the chassis radiator. The cooler shall permit the use of water from the pump for cooling system. The cooling shall be done without mixing engine and pump water.

WATER LEVEL GAUGE

The water tank shall be equipped with a Class 1, Model # ITL, Itelli-Tank water tank level gauge for indicating water level on the pump operator's panel. The tank level gauge shall indicate the liquid level on a four light, easy to read display and show increments of 1/20 of a tank.

The gauge shall use a pressure transducer installed near the bottom of the water tank to determine the correct volume in the tank.

A Class One remote relay module shall be provided to provide outputs for large indicator lights on the side of the vehicle.

LARGE LIGHT WATER LEVEL GAUGE, EACH SIDE OF CAB

A large light water level gauge system shall be provided on both sides of the cab. Each side shall be provided with four (4) Whelen 500 series LED lights mounted behind the rear crew door above the handrail. The lights shall be surface mounted on the sides of the cab.

The lights shall be mounted as to indicate the following water levels:

- Top light with green lens	Full tank

- Second light with blue lens	3/4 tank

- Third light with amber lens	1/2 tank

- Fourth light with red lens	1/4 tank

The fourth light shall burn steady red to indicate 1/4 tank and shall start to flash when the water level drops below 1/4 tank. To prevent distraction to drivers, this tank level gauge shall be wired to display only when the park brake is engaged.

FOAM TANK LEVEL GAUGE - FOAM TANK "A"

The foam tank shall be equipped with a Class 1, Model # ITL, Itelli-Tank level gauge for indicating foam level on the pump operator's panel. The tank level gauge shall indicate the liquid level on a four light, easy to read display and show increments of 1/20 of a tank.

The gauge shall use a pressure transducer installed near the bottom of the foam tank to determine the correct volume in the tank.

MICROPHONE BOX/SPEAKER GRILLE

A stainless steel 12" wide x 8" high x 6" deep microphone box with an integral speaker grille and spring loaded door shall be provided.

The microphone box shall be recessed in an applicable location determined at the Pre-construction meeting.

WATER TANK

The water tank shall have a capacity of 2500 gallons, constructed from polypropylene material.

FOAM TANK "A"

Included in the total capacity of the water tank, a 30 gallon integral foam storage area shall be built into the water tank. The foam tank shall have a latched fill tower, properly labeled as the foam fill point. A valved drain shall be provided.

The Poly water tank shall be constructed from 1/2" thick polypropylene sheet stock. This material shall be a non corrosive stress relieved thermo-plastic, natural in color, and U.V. stabilized for maximum protection.

The water and foam tanks shall be of a specific configuration and is also designed to be completely independent of the body and compartments. All joints and seams shall be nitrogen welded and tested for maximum strength and integrity. The top of the booster tank is fitted with removable lifting eyes designed with a 3 to 1 safety factor to facilitate easy removability. The transverse swash partitions shall be manufactured of 3/8" polypropylene (natural in color) and extend from approximately 4" off the floor to just under the cover. The longitudinal swash partitions shall be constructed of 3/8" polypropylene (natural in color) and extend from the floor of the tank through the cover to allow for positive welding and maximum integrity. All partitions shall be equipped with vent and air hoses to permit movement of air and water between compartments. The partitions shall be designed to provide maximum water flow. All swash partitions interlock with one another and are welded to each other as well as to the walls of the tank.

TANK LID

The tank cover shall be constructed of 1/2" thick polypropylene, natural in color, and U.V. stabilized, to incorporate a multi three-piece design, which allows for individual removal and inspection if necessary. The tank cover shall be recessed 3/8" from the top of the tank and shall be welded to both sides and longitudinal partitions for maximum integrity. Each one of the covers shall have hold downs consisting of 2" polypropylene dowels spaced a maximum of 30" apart. These dowels shall extend through the covers and become welded to the transverse partitions. This shall assist in keeping the cover rigid under fast filling conditions. A minimum of two lifting dowels shall be drilled and tapped 1/2" X 13" to accommodate the lifting eyes.

TANK FILL TOWER

The tank shall have a combination vent and manual fill tower. The fill tower shall be constructed of 1/2" polypropylene and shall be 12" W x 36" L outer perimeter. The tower shall be located a minimum of 6" off the front wall and 10" off either of the side walls. The tower shall have a 1/4" thick removable polypropylene screen and a polypropylene hinged type cover. The fill tower cover shall be marked as a water tank fill point.

OVERFLOW AND VENT PIPE

The fill tower shall be fitted with an integral 6" I.D. schedule 40 P.V.C. combination overflow/vent pipe running from the fill tower through the tank to a 6" coupling flush mounted into the bottom of the tank to allow water to overflow behind the chassis rear axle.

TANK SUMP

The tank sump shall be a minimum of 10" wide x 10" long x 3" deep. An anti-swirl plate shall be mounted inside the sump, approximately 1" above the bottom of the sump.

TANK SUMP CONNECTION

The front bulkhead of the water tank shall be fitted with one (1)

A 3" drain plug shall be provided.

OUTLETS

There shall be two (2) standard tank outlets; one for tank-to-pump suction line which shall be a minimum of 4" coupling and one for a tank fill line which shall be a minimum of a 2" N.P.T. coupling. All tank fill couplings shall be backed with flow deflectors to break up the stream of water entering the tank.

TANK MOUNTING

The tank shall rest on the body cross members spaced a maximum of 22" apart, and shall be insulated from these cross members with a minimum of 3/8" nylon webbing or 1/2" rubber, 2-1/2" wide. The tank shall sit cradle-mounted using four (4) corner angles of 6 x 6 x 4 x 0.250 welded directly to the body cross members. The angles shall keep the tank from shifting left to right or front to rear. The tank is designed on the free-floating suspension principle and shall not require the use of hold downs. The tank shall be completely removable without disturbing or dismantling the apparatus body structure. The hose bed cross braces shall act as water tank retainers.

10" NEWTON STAINLESS STEEL DUMP - REAR

The rear of the water tank shall be equipped with a 10" Newton Stainless Steel Dump Valve, Model #1060-34 with a left side mounted manual actuation lever. The dump valve setup shall be capable of discharging the water tank contents at a rate of at least 1800 G.P.M.

NEWTON STAINLESS STEEL 36" MANUAL TELESCOPING CHUTE

The rear Newton Dump shall be equipped with a Newton Model #4036-34, 36" manual telescoping, stainless steel dump chute.

DIRECT TANK FILL - DRIVER SIDE

One (1) 2-1/2" NST direct tank fill shall be provided at the rear of the body, on the driver side, as low as possible. The direct tank fill shall be gated with a 3" Akron ball valve with a swing handle. The fill shall be equipped with a 30 degree elbow terminating with a 2-1/2" NST female swivel connection. A quarter turn drain valve shall be supplied to bleed off excess pressure with a drain hose routed beneath the rear step area.

DIRECT TANK FILL - OFFICER SIDE

One (1) 2-1/2" NST direct tank fill shall be provided at the rear of the body, on the officer side, as low as possible. The direct tank fill shall be gated with a 3" Akron ball valve with a swing handle. The fill shall be equipped with a 30 degree elbow terminating with a 2-1/2" NST female swivel connection. A quarter turn drain valve shall be supplied to bleed off excess pressure with a drain hose routed beneath the rear step area.

APPARATUS BODY DESIGN CONSTRUCTION

The body side and compartment assemblies shall be designed and assembled to provide maximum strength and durability under all operating conditions.

Special attention shall be taken to minimize corrosion on all fabricated parts and structural members of the body. All bolt-on components shall be provided with a dissimilar metals isolation barrier to prevent electric corrosion. The body design shall also incorporate removable panels to access spring hangers, rear body mounts and fuel tank sending units.

The body assembly shall be an all-welded configuration. The body shall be completely isolated from the cab and pump module structure.

BODY AND COMPARTMENT FABRICATION - STAINLESS STEEL

All compartment panels and body side sheets shall be entirely 12 gauge stainless steel (Type 304L). Each side compartment assembly shall be both spot welded and stitch welded to ensure proper weld penetration on all panels while avoiding the possible warping caused by a full seam weld. The side compartments shall be welded on a fixture to ensure true body dimensions of all door openings. The side compartments and body side panels are then set into a body squaring fixture where the super structure is installed and the entire body is aligned to be completely symmetrical. The super structure is then welded to the compartment side panels and reinforcement plates are inserted which allows the compartment panels to become an integral component of the body support structure. A full seam weld shall not be used to the applied heat which shall distort sheet metal and remove the protective coating from the perimeter of the welded area. All seams shall be caulked prior to finish paint to ensure proper compartment seal.

100" WIDE FIRE BODY

The fire body shall be 100" wide to provide the maximum amount of usable hose bed space, approximately 76" wide, and to extend the body fenderettes outward for better tire tread coverage. All lower compartments shall be 26" deep overall, all upper compartments shall be 12" deep overall.

SUPER STRUCTURE - STAINLESS STEEL

The body super structure shall be an all welded configuration utilizing a combination of 3” x 1-1/2” Type 304 structural grade tubing and Type 304 structural channel.

The super structure shall be designed to totally support the full length and width of the body. The structure shall be welded to the body side compartments to incorporate the compartments into an integral part of the body weldment.

The super structure shall be bolted to the sides of the chassis frame at four (4) points.

STEPPING, STANDING, & WALKING SURFACES

All stepping, standing, and walking surfaces on the body shall meet NFPA #1901 anti-slip standards. Aluminum tread plate utilized for stepping, standing, and walking surfaces shall be Alcoa No Slip type. This material shall be certified to meet the NFPA #1901 standard. Upon request by the Purchaser, manufacturer shall supply proof of compliance with this requirement. (There shall be No Exceptions allowed for this paragraph)

DRIVERS SIDE COMPARTMENTATION

One (1) full height/split depth compartment, with a vertically hinged double door, forward of the rear wheels. Compartment dimensions 68” High x 49” Wide, with a door opening of 67” High x 46” Wide.

One (1) full height/split depth compartment, with a vertically hinged double door, behind the rear wheels. Compartment dimensions 68” High x 55” Wide, with a door opening of 67” High x 52” Wide.

One (1) high side compartment, with a horizontally hinged door, over the rear wheels. Compartment dimensions 32” High x 109” Wide, with two (2) door openings each 29-1/2” High x 50” Wide.

OFFICERS SIDE COMPARTMENTATION

One (1) full height/split depth compartment, with a vertically hinged double door, forward of the rear wheels. Compartment dimensions 68” High x 49” Wide, with a door opening of 67” High x 46” Wide.

One (1) full height/split depth compartment, with a vertically hinged double door, behind the rear wheels. Compartment dimensions 68” High x 55” Wide, with a door opening of 67” High x 52” Wide.

One (1) high side compartment, with a horizontally hinged door, over the rear wheels. Compartment dimensions 32” High x 109” Wide, with two (2) door openings each 29-1/2” High x 50” Wide.

COMPARTMENT DOORS

The compartment doors shall be flush type with the outer skin fabricated from 3/16" (5052 H32) aluminum. The door skin shall have a formed flange on one (1) side used as a hinge mounting flange. The door skin shall have reinforcing channels welded internally which accommodate the inner door pan mounting.

The 2" thick compartment doors shall reduce the overall specified compartment depth by 2".

All horizontally hinged doors shall be 1" thick to provide additional compartment storage area. The 1" thick horizontally hinged doors shall reduce the overall specified compartment depth by 1-1/4".

DOOR LINER

Each inner pan shall be constructed from 1/8" aluminum material, which shall be provided with a brushed finish. The brushed finish shall allow the fire department to remove scratches from the inner door pan with sand paper or scuff pad. Each inner door pan shall be fastened to the door frame channels to provide a smooth, snag-free inner door surface. The inner door pan on the running board compartments shall enclose the latch and reinforcements completely. The pan shall be easily removable to access the enclosed latch mechanism.

HINGES

Hinges shall be full length polished stainless steel piano type. The hinges shall be mounted with stainless steel hardware.

DOOR SEALS

Enclosed body compartment doors shall be equipped with a closed cell gasket. The gasket material shall be EPDM to provide a gasket resistant to weather, temperature extremes, and aging.

DOOR LATCHES – ROTARY WITH D-RINGS

Externally latched body doors shall be equipped with stainless steel D-ring handles.

Rotary door latches shall be provided for all full height body doors, which shall incorporate rotary latches at the top and bottom of all externally latched single or double doors. Linkages shall be provided between the actuation handle and the latch mechanisms.

The blank door of a double door configuration shall have rotary latches at the top and bottom of each door with the latch release lever accessible thru the door frame, which eliminates the need to reach inside the compartment to release the door. Linkages shall be provided between the actuation handle and the latch mechanisms.

Horizontally hinged doors shall be equipped with a single rotary door latch.

STAY ARMS

Stay arms shall be "Cleveland" double acting style, to be used on all vertically hinged storage compartment doors.

All horizontally hinged compartment doors shall be furnished with two (2) Eberhard gas shock type door stay arms.

SWEEP-OUT COMPARTMENT FLOORS

Compartment floors shall be welded to the compartment walls and have a sweep out design for easy cleaning.

Compartments with hinged doors shall have the door opening flanges bend down to produce the sweep-out design.

Compartments with roll-up style doors shall have the external floor flange stepped down, 1/2" high x 2" deep, to produce a sealing surface for the roll-up doors below the compartment floor. The sweep out design shall also permit easy cleaning.

Compartments set on running boards, which could cause additional corrosion potential, are not acceptable.

A 90° angle door sill protector, fabricated from 18 gauge brushed finish stainless steel shall be installed on the bottom external edge of each body compartment door opening to help protect this area from paint chipping.

BEAVERTAILS

The rear body beavertail area shall be furnished with a squared off appearance to maximize the available compartment area, while providing added support to the rear step support structure. The beavertail panels shall be assembled in conjunction with the rear body corner panels. This assembly shall provide a vertical mounting surface for tail lights at the rear most portion of the body and additional storage space.

The inside of the beavertails shall be furnished with polished aluminum tread plate overlays.

COMPARTMENT TOPS

Compartment tops shall be covered with polished aluminum tread plate on both sides.

DRIP MOLDING

Compartment tops over all side compartments shall have a 45 degree flange formed out to provide protection against water runoff. A secondary extruded drip molding shall be provided between low compartments and auxiliary high side compartments, when auxiliary compartments are provided.

FASTENERS

All exterior fasteners used for holding panels or tread plate shall be stainless steel. In no case shall pop rivets or self-tapping screws be used.

COMPARTMENT LOUVERS

Machine stamped ventilating louvers shall be furnished in each compartment, and so located that water cannot normally enter the compartment.

A perforated, polished, stainless steel grille shall be furnished between compartments for ventilation in the event that the compartment configuration does not allow louvers to ventilate to the atmosphere.

ACCESS PANELS

Removable access panels shall be provided in all lower compartments to access spring pins, fuel tank sender, electrical junction compartment and rear body mounts.

Protective panels shall be located in the rear compartments providing access to the lights and associated wiring. The covers shall also serve as protective covers to prevent inadvertent damage to lights or wiring from tools or equipment located in the compartment.

REAR BODY PANEL

The rear body panel shall be fabricated from a minimum of 3/16" polished aluminum tread plate and shall extend the full width between the beavertails. This panel shall be full height from the rear step to the hose bed floor. The panel shall be bolted on and removable, with no part of the rear panel attached to the booster tank.

BODY RUB RAILS (BRUSHED STAINLESS STEEL)

Sacrificial, brushed finish, stainless steel rub rails shall be mounted at the base of the body, extend outward a minimum 3/4", downward 2" and flange inward 1". The rub rails shall extend the full length of the main body and wrap around the rear body corners. Rub rails shall be designed to bolt to the body from the bottom side of the compartment area, so as not to damage the body side panels on initial impact and to provide for ease of replacement.

RUNNING BOARD STEPS

The driver and officer running board steps shall be fabricated of 3/16" polished aluminum tread plate. The outside edge on each step shall be fabricated with a double break, return flange. The steps shall be rigidly reinforced with a heavy duty support structure. The running boards shall not form any part of the compartment design, and shall be bolted into place with a minimum 1/2" clearance gap between any panel to facilitate water runoff.

OFFICER SIDE RUNNING BOARD STORAGE WELL

A storage well, constructed of 1/8" aluminum, shall be recessed into the officer’s side running board. The storage well shall measure 9" deep x 9" wide x as long as possible between the running board support members. Drain holes shall be located in the bottom corners to allow water to drain from the storage well.

The officer's side running board hose well shall be furnished with velcro straps to secure the hose stored in the well. The straps shall be attached to each side of the hose well with stainless steel footman loops.

The officer’s side storage well shall be equipped with Dri-Deck material to provide drainage and ventilation of equipment in storage well.

DRIVER SIDE RUNNING BOARD STORAGE WELL

A storage well, constructed of 1/8" aluminum, shall be recessed into the driver’s side running board. The storage well shall measure 9" deep x 9" wide x as long as possible between the running board support members. Drain holes shall be located in the bottom corners to allow water to drain from the storage well.

The driver's side running board hose well shall be furnished with Velcro straps to secure the hose stored in the well. The straps shall be attached to each side of the hose well with stainless steel footman loops.

The driver’s side storage well shall be equipped with Dri-Deck material to provide drainage and ventilation of equipment in storage well.

REAR STEP

The rear step shall be sixteen (16) inches deep, with twelve (12) inches recessed between the rear portion of the rear side compartments and an additional four (4) inches extended beyond the rear of the body. The step shall be fabricated from 3/16" polished aluminum tread plate, and shall be rigidly reinforced. The recessed portion of the step shall be 52" wide.

The rear edge of the step shall be designed to accommodate the rear clearance lights, recessed for protection in the step reinforcement channel. This step shall be bolted into place with a minimum 1/2" clearance gap between it and the body panel.

INTERMEDIATE REAR STEP

An eight (8) inch deep, bolt on intermediate rear step, fabricated from 3/16" aluminum tread plate, shall be installed. The step shall be approximately 8" deep x 48" wide.

REAR STEP COMPARTMENT

One (1) rear step compartment shall be provided between the frame rails. This compartment shall be as tall, wide and deep as possible in the given area. This shall vary based on frame width, frame height and depth of rear cross member. The compartment shall have a hinged tread plate door with a D-ring handle automotive latch.

GRAB RAILS

All hand rails shall be 1-1/4" outer diameter, knurled bright anodized aluminum extrusion, designed to meet NFPA 1901 requirements.

Molded gaskets shall be installed between the handrail stanchion castings and body surfaces to prevent electrolytic reaction between dissimilar metals and to protect paint.

GRAB RAIL LOCATIONS:

Two (2) vertical rails shall be mounted on the rear edge of the beavertails, one (1) each side.

One (1) horizontal, full width handrail shall be installed on the rear, below the level of the hose bed.

FOLDING STEPS - REAR OF BODY

Four (4) Austin Hardware Model FS-200 CHR large folding steps, made of high strength die cast aluminum, with a textured chrome plate finish, minimum of 42 in² surface, conforming to NFPA-1901 requirements, shall be provided on the rear of the body, two (2) each side. The steps shall be mounted to accommodate access to the body hosebed area with a maximum of 18" height between each step.

SAFETY SIGN(S) AT REAR STEP AND CROSS WALKWAY(S)

Safety sign(s) shall be located on the vehicle at the rear step, and at any cross walkway(s), to warn personnel that riding in or on these areas while the vehicle is in motion is prohibited.

REAR WHEEL WELL LINERS

Fully removable, bolt-in, 1/8" aluminum fender liners shall be provided. The wheel well liners shall extend from the outer wheel well body panel, into the truck frame. Removable vertical splash shields, inward of the wheels, shall be provided to give access to the hydraulic components. The completely washable fender liners shall be designed to protect the front and rear compartments and main body supports from road salts, dirt accumulation and corrosion. Fender liners which are welded in place or are only partially removable shall not be considered.

REAR FENDERETTES

The tandem rear fenders shall be equipped with easily replaceable, polished stainless steel fenderettes. The fenderettes shall be equipped with a rubber gasket molding between the body panel and the fender. Integral welded crown type liners shall not be acceptable.

AIR BOTTLE STORAGE COMPARTMENTS

A total of eight (8) SCBA air bottle storage compartments (8" high x 8" wide x 26" deep) shall be inserted into the body fender area on a 5 degree pitch. The compartments shall be located with three (4) on the driver side and four (4) on the officer side of the rear body fender panels. The lower portion of the compartments shall be non-abrasive to absorb shock and help secure the bottle.

Each storage compartment shall be equipped with a polished stainless steel door.

MUD FLAPS, REAR

Heavy duty mud flaps shall be provided behind the rear wheels.

REAR TOW EYES

Two (2) painted tow eyes shall be furnished on the rear of the vehicle, extending through the rear body panel. The tow eyes shall be made from plate steel and shall be bolted directly to the chassis frame rails with grade 8 bolts. The tow eyes shall be smooth and free from sharp edges, and have a minimum eyelet hole of 2-1/2". The tow eyes shall be painted.

HOSE BED

The hose bed shall be located directly above the booster tank and shall be free from all sharp objects such as bolts, nuts, etc., to avoid damage to fire hose.

The hose bed storage area, shall have a minimum capacity of sixty (60) cubic feet, and shall accommodate 2-1/2" or larger fire hose as required by the Purchaser. The hose bed depth shall be 10".

The hose bed shall be located directly above the booster tank and shall be free from all sharp objects such as bolts, nuts, etc., to avoid damage to fire hose.

For added strength, rigidity and appearance, the hose bed side walls shall have the top edge flanged outward two (2) inches and downward one (1) inch. In a similar fashion, the top edge of the front wall shall be flanged inward two (2) inches and downward one (1) inch.

HOSE BED FLOORING

Flooring to be constructed from extruded aluminum and be properly spaced for ventilation. The flooring shall be smooth and free from sharp edges to avoid hose damage. The hose bed floor shall be removable to provide access to inner body framework.

HOSE BED PARTITIONS

Two (2) fully adjustable 3/16", brushed finish, aluminum hose bed partitions shall be provided. Partitions shall be easily adjustable by means of uni-strut channels located at the front and rear of the hose bed. Partitions shall be removable for access to the booster tank.

VINYL HOSE BED COVER - 1/4 TURN FASTENERS

A hose bed cover shall be provided and installed. The cover shall be made from 22 ounce; heavy-duty vinyl coated polyester fabric (TXN 226). The cover shall be sewn with ultraviolet resistant thread and shall have 2" wide nylon webbing sewn around the perimeter to provide additional strength.

The cover shall be secured to the top front body flange with quarter-turn fasteners. The cover shall be secured to the side body flanges with quarter-turn fasteners. A weighted flap shall be furnished on the rear of the cover with two (2) bungee cords.

The Hypalon material shall be red in color.

ADJUSTABLE SHELVING

Compartment shelving shall be constructed of 3/16” brush finish aluminum with a 2” upward bend at front and rear, and side supports. Shelving shall be vertically adjustable with spring nuts in aluminum strut channel.

Adjustable shelves shall be located as follows:

Four (4) adjustable shelf(s) shall be provided and mounted as directed by the fire department.

500 POUND FLOOR MOUNTED ROLL OUT TRAYS

Floor mounted roll-out trays shall consist of heavy duty, roller bearing slide tracks with an end load rating of 500 pounds, securely fastened to the compartment floor. The tray shall be fabricated from 3/16" brushed aluminum with a minimum 2" high flange on each of the four sides to assist in retaining the equipment stored on each tray. The slide tracks shall have a 100% extension, allowing the tray to extend out of the compartment completely.

The 500 pound floor mounted roll out trays shall be located as follows:

Four (4) roll out tray(s) shall be provided and mounted as directed by the fire department.

HYDRAULIC REEL

One (1) Hannay, Model 2016-17-18 electric rewind Hydraulic reel(s) with a capacity of 100 feet of twin hydraulic hose shall be provided and mounted at a location determined by the customer.

One (1) Hannay 4-way stainless steel roller assembly(s) shall be provided on the specified hydraulic reel(s). The roller assembly opening shall be the full width of the reel drum. Support brackets for the roller assembly shall be bolted to the hose reel.

One hundred feet (100') of Parker, high pressure, twin hydraulic hose for Hurst equipment shall be provided on the hydraulic reel.

120/240 VOLT ELECTRICAL SYSTEM TESTING

All line voltage wiring and permanently connected devices and equipment shall be subjected to a dielectric voltage withstand test of 900 volts for one minute. The test shall be conducted between live parts and the neutral conductor and between live parts and the vehicle frame with any switches in the circuits closed. The test shall be conducted after all bodywork has been completed. The dielectric tester shall have a minimum 500 VA transformer with a sinusoidal output voltage that can be verified.

Electrical polarity verification shall be made of all permanently wired equipment and receptacles to determine that connections have been properly made.

OPERATIONAL TESTING

The apparatus manufacturer shall perform the following operation test and shall certify that the power source and any devices that are attached to the line voltage electrical system are properly connected and in working order.

The generator shall be started from a cold start condition and the line voltage electrical system shall be loaded to 100 percent of the nameplate voltage rating.

The following items shall be monitored and documented every 15 minutes:

- The cranking time until the generator starts and runs.

- The voltage, frequency, and amperes at continuous full rated load.

- The generator oil pressure, water temperature, transmission temperature, hydraulic temperature, and the battery rate charge, as applicable.

- The ambient temperature and altitude.

The generator shall operate at 100 percent of its nameplate wattage for a minimum of two (2) hours.

HARRISON 20,000-WATT HYDRAULIC DRIVEN GENERATOR

One (1) Harrison Hydraulic Driven Generator Mdel number 20.0MPC-16D rated at 20000 watts, 83/167 amps, 120/240VAC, 60 Hz, 1-phase shall be provided.

The system shall be designed and assembled by a company with no less than 10 years experience in the manufacture of hydraulic driven generators. The system shall be tested at the full nameplate load prior to shipping and be accompanied with the test report. The test report shall document the generators performance at various loads from no load to full load to ensure reliable power delivery at those loads.

The motor/generator shall be placed in a frame which affords protection to the components and provides a unitized mounting module containing the motor/generator, reservoir, oil cooler, filtration, manifold containing a cross port check valve and relief valve.

The generator shall be a continuous duty, industrial type with a heavy-duty bearing and of brush less design to ensure low maintenance. No brushes or slip rings shall be allowed. The reservoir shall include an oil level sight gauge, oil temperature gauge; fill cap, oil filter, low fluid level sensor, high temperature sensor and a venturi boost unit to provide positive pressure to the pump suction port. The generator and motor shall be close coupled and aligned using a single bearing alternator design. No two (2) bearing generators shall be permitted.

The system must be capable of producing the full nameplate power when driven from the vehicle PTO from idle to maximum engine speed. The generator system must be able to operate on either a Constant Engaged PTO or a Hot Shift PTO. Determination as to which PTO to use shall be made by the Fire Department. The generator must be able to be used while vehicle is either stationary or in motion.

The hydraulic motor and pump shall be of axial piston design to provide low internal leakage and a high degree of frequency stability. No gear pumps or motors shall be used. The pump shall match the system with the proper orifice, pressure compensator, and load sense settings to provide stable output regardless of engine rpm or electrical load demands.

The system shall be capable of normal operations using a commonly available ATF fluid, such as GM Dextron III or equivalent. All fluid service points shall be in close proximity to the reservoir for ease of scheduled maintenance.

When properly installed, the system shall be warranted for a period of not less than two (2) years or 2000 hours, whichever should come first.

A weatherproof digital Quadra meter containing the volt, amp, and frequency shall be installed near the breaker panel.

GENERATOR PTO

A hot shift PTO shall be provided on the transmission for the Harrison generator. The PTO shall be controlled from the cab. The control shall include a PTO engagement switch and a PTO engaged indicator light.

GENERATOR WARRANTY

The specified generator shall have a two (2) year or two thousand (2000) hour warranty as provided by the generator manufacturer. A copy of the generator warranty shall be provided at time of delivery.

The generator shall be mounted above the pump enclosure on the driver side.

Locating the generator greater than 144" from the main breaker panel may require the installation of an additional power disconnecting means.

LOAD CENTER

The generator output line conductors shall be wired from the generator output connections to a Square D, model #QO120L125G breaker panel. The breaker panel shall be equipped with a properly sized main breaker using two (2) of the twenty (20) spaces which leaves a total of eighteen (18) available spaces.

The generator output conductors shall be sized to 115% of the main breaker rating and shall be installed as indicated in the wiring section.

Eighteen (18) appropriately sized, 120 volt, circuit breakers shall be provided.

The breaker panel shall be located on the rear wall of the driver side upper compartment.

WIRING METHODS

Wiring/conduit shall not be attached to any chassis suspension components, water or fuel lines, air or air brake lines, fire pump piping, hydraulic lines, exhaust system components or low voltage wiring.

All wiring shall be installed at a minimum of 12 inches away from any exhaust piping and a minimum of 6 inches from any fuel lines.

All wiring shall be securely clamped within 6 inches of any junction box and at a minimum of every 24 inches of run. All supports shall be of nonmetallic material or corrosion protected metal. All supports shall not cut or abrade conduit or cable and shall be mechanically fastened to the vehicle.

All power supply assembly conductors, including neutral and grounding conductors, shall have an equivalent amperage rating and shall be sized to carry not less than 115% of the main breaker rating.

All Type SO or Type SEO cable not installed in a compartment shall be installed in wire loom. Where Type SO or Type SEO cable penetrates a metal surface, a rubber or plastic grommet or bushing shall be provided.

The installation of all 120/240 wiring shall meet the current NFPA-1901 Standards (NO EXCEPTIONS).

WIRING IDENTIFICATION

All line voltage conductors located inside the main breaker panel box shall be individually and permanently identified. When pre-wiring for future power wiring installations, the non-terminated ends shall be labeled showing function and wire size.

GROUNDING

The neutral conductor of the power source shall be bonded to the vehicle fame only at the power source.

The grounded current carrying conductor (neutral) shall be insulated from the equipment grounding conductors and from the equipment enclosures and other grounded parts. The neutral conductor shall be colored white or gray.

In addition to the bonding required for the lower voltage return current, each body and driving/crew compartment enclosure shall be bonded to the vehicle frame by a copper conductor. The conductor shall have a minimum amperage rating of 115 percent of the name plate current rating of the power source specification label.

CIRCUIT BREAKER/RECEPTACLE INSTALLATION

The system shall be installed by highly qualified electrical technicians to assure the required level of safety and protection to the fire apparatus operators. When multiple circuit are required, the circuits shall be wired to the breaker panel in a staggered configuration to minimize electrical loads on each breaker or generator (leg) circuit. The wiring, electrical fixtures and components shall be to the highest industry quality standards available on the domestic market. The equipment shall be the type as designed for mobile type installations subject to vibration, moisture and severe continuous usage.

RECEPTACLE INSTALLATIONS

Any receptacle installed in a wet location must be a minimum of 24 inches above the ground and provided with an approved wet location cover. Wet receptacles may not be mounted at more than 45 degrees from vertical, nor can they be mounted in a face-up position.

One (1) 110 volt, NEMA L5-20, 20 amp, Single twist-lock receptacle with a grey thermoplastic, corrosion resistant, weatherproof cover shall be installed as directed by the fire department.

This receptacle shall require one (1) 20 amp, 110 volt circuit breaker to be installed in the load center.

One (1) 220 volt, NEMA L6-30, 30 amp, single twist-lock receptacle with a grey thermoplastic, corrosion resistant, weatherproof cover shall be installed as directed by the fire department.

The receptacle shall require one (1) 30 amp, 220 volt circuit breaker to be installed in the load center.

ELECTRIC CORD REELS (220 VOLT)

Two (2) Hannay Model #ECR-1618-17-18, with 4 conductor collector assembly for 220 volts, with electric rewind cord reels shall be provided and wired to the breaker panel. The reels shall be securely mounted and equipped with a rewind control adjacent to each reel.

The cord reels shall be mounted as directed by the fire department.

The circuit breaker used to protect any device attached to the cord reel shall be sized to the smallest electrical connection used.

ELECTRIC CABLE

Two hundred (200) feet of Type SO black 10/4 heavy duty electric cable, wired for 220 volt, shall be provided on each of the cord reels.

Two (2) NEMA L14-20R, 20 amp, four prong twist-lock receptacle(s) shall be provided on the end of the cable.

JUNCTION BOX(ES)

One (1) Akron Model EJB-GFCI, four (4) outlet junction box(es) with one (1) NEMA 5-20R GFCI rated straight blade receptacle and three (3) NEMA L5-20R twist-lock receptacles with 12" pigtail with a NEMA L14-20P twist-lock plug shall be provided.

The junction box shall be wired such that the two (2) outlets provide 120 VAC.

CABLE ROLLER ASSEMBLY

Two (2) four (4) roller assembly(s) shall be provided adjacent to each cord reel to provide un-obstructed deployment and rewinding of the cable.

Two (2) cable ball stop(s) shall be installed on the cable to keep the cable end from passing through the roller assembly.

LIGHTING (AS DIRECTED ON CAB)

Two (2) Fire Research FOCUS, Model #FC200, shall be recessed, and installed on the cab as directed by the Fire Department using the FOCUS custom castings. The recess casting shall incorporate internal heat dissipating fins. The bulb shall be accessible through the front glass and frame which is fastened to the lamp assembly by four Phillips head screws. The flush mount housing shall be no more than 2" in depth.

Each Fire Research light shall be equipped with a 500 watt Model S50, FOCUS™ lamp head. The small, low-profile lamp head shall be no larger than 3.5" high and shall actively direct 50 percent of the light from a quartz bulb onto the action area while still providing 50% illumination in the working area. The bulb shall be easily accessible through the front glass and frame. Changing the bulb should be easily done from the front of the lamp head. The glass and frame must be removable, held onto the lamp assembly by no more than four front screws.

Two (2) Model S50, 500 watt light heads shall require one (1) 120V, 15 amp circuit breaker.

LIGHTING (RECESSED REAR OF BODY)

Two (2) Fire Research FOCUS, Model #FC200, shall be recessed, on the rear face of the body, one (1) each side using the FOCUS custom castings. The recess casting shall incorporate internal heat dissipating fins. The bulb shall be accessible through the front glass and frame which is fastened to the lamp assembly by four Phillips head screws. The flush mount housing shall be no more than 2" in depth.

Wiring used for the lighting shall be a minimum of 16 gauge three (3) wire cable that is properly supported and protected from damage.

Each Fire Research light shall be equipped with a 500 watt Model S50, FOCUS™ lamp head. The small, low-profile lamp head shall be no larger than 3.5" high and shall actively direct 50 percent of the light from a quartz bulb onto the action area while still providing 50% illumination in the working area. The bulb shall be easily accessible through the front glass and frame. Changing the bulb should be easily done from the front of the lamp head. The glass and frame must be removable, held onto the lamp assembly by no more than four front screws.

Two (2) Model S50, 500 watt light heads shall require one (1) 120V, 15 amp circuit breaker.

CAB BROW LIGHTING

One (1) Fire Research FOCUS, Model #FCA800 contour mount brow light(s) shall be provided. The entire assembly shall be UL listed as Scene light for Fire Service Use, manufactured by Fire Research.

The light(s) shall be mounted on the upper forward face of the cab. Wiring used for the lighting shall be a minimum of 16 gauge three (3) wire cable that is properly supported and protected from damage.

The Fire Research light shall be equipped with a 1000 watt Model M10, FOCUS™ lamp head. The small, low-profile lamp head shall be no larger than 3.5" high and shall actively direct 50 percent of the light from a quartz bulb onto the action area while still providing 50% illumination in the working area. The bulb shall be easily accessible through the front glass and frame.  Changing the bulb should be easily done from the front of the lamp head. The glass and frame must be removable, held onto the lamp assembly by no more than four front screws.

One (1) Model M10, 1000 watt light head shall require one (1) 120V, 15 amp circuit breaker.

QUARTZ LIGHTS REAR OF BODY SWITCHING

The quartz lights on the rear of the body shall be wired through the circuit breaker panel and switched at the cab dash or overhead. The control switches shall be wired through low voltage relays to maintain 12 volt circuits in the cab.

QUARTZ LIGHTS MOUNTED ON CAB SWITCHING

The quartz lights on the cab shall be wired through the circuit breaker panel and switched at the cab dash or overhead. The control switches shall be wired through low voltage relays to maintain 12 volt circuits in the cab.

BROW LIGHT SWITCHING

The quartz light above the windshield shall be wired through the circuit breaker panel and switched at the cab dash or overhead. The control switches shall be wired through low voltage relays to maintain 12 volt circuits in the cab.

WILL-BURT NIGHTSCAN LIGHT TOWER

A Will-Burt Nightscan 3.0, Model NS 3.0-RCP-9000 OP surface mounted light tower shall be provided and mounted as specified.

The light tower shall be equipped with six (6) 1500-watt, 240-volt quartz halogen FRC Optimum light fixtures to provide a total of 9,000 watts of lighting. The light tower uses an RCP (Remote Control Positioner) attached to the end of the mast to allow full rotation and independent tilt (Dual Tilt) of the right and left light banks at any vertical height to ensure total scene coverage in two separate directions. The light tower extends to a maximum height of eleven (11) feet from the mounted surface and auto stows to a maximum height of 13.5 inches from the mounted surface. A 12 volt vertical look-up light shall be provided on the light tower base to automatically illuminate the operational envelope of the mast.

The light towers functions including "auto stow," are operated by a pistol grip remote control hardwired into the tower. The remote control shall be mounted in a body compartment as specified.

The six (6) 1500-watt light heads shall require two (2) 240-volt, two pole 20-amp circuit breakers.

The light tower shall be mounted at the front of the hose bed.

LADDER STORAGE RACK (OFFICER SIDE)

An electronically controlled swing down ladder rack, manufactured by the Ziamatic Corporation, shall be provided. The ladders shall be stored vertically above the compartments on the officer side of the apparatus. The Ziamatic ladder rack is operated by two (2) Warner Electric linear actuators. Each actuator includes a built in safety slip clutch.

The actuator switch for the ladder rack shall be located on the officer side pump panel area in an enclosed housing, whereas the operator shall have full view of the rack during the raising or lowering operation. A warning alarm shall activate when the rack is in motion, the warning light shall be installed on the officer side rear body panel. A flashing warning light shall be provided on the cab dash to indicate when the rack is not in the raised travel position. An interlock system shall be provided whereas if any compartment door on the officer side of the body is open, the rack shall not operate.

LADDERS

The following Duo-Safety ground ladder compliment shall be provided:

One (1) Duo-Safety series 1225-A, 35', aluminum, three (3) section extension ladder shall be provided.

One (1) Duo-Safety series 775-A, 14', aluminum, straight roof ladder with folding hooks shall be provided.

One (1) Duo-Safety series 585-A, 10', folding, aluminum, attic ladder shall be provided.

PIKE POLE STORAGE

One (1) pike pole tube(s) shall be provided. Each holder shall be equipped with a spring type holder and shall be accessible from the rear of the apparatus. Each pike pole holder shall be labeled to indicate the pike pole length.

The pike pole tube(s) shall be mounted on the ladder rack.

PIKE POLE

A six (6) foot fiberglass handled pike pole with mounting brackets shall be furnished.

PIKE POLE

A ten (10) foot fiberglass handled pike pole with mounting brackets shall be furnished.

SUCTION HOSE STORAGE

The suction hose shall be located in an area as directed by the fire department.

SUCTION HOSE

Two (2) 10 foot sections of six (6) inch PVC lightweight suction hose shall be furnished (Kochek or Firequip Maxi-Flex). Suction hose shall be for suction only and not to be used on pressurized hydrants or for relay pumping. Couplings shall include a long handle, female swivel on one end and a rocker lug male on the other end. All threads shall be six (6) inch N.S.T.

NOTE: All PVC suction hoses are strictly drafting hoses and must not be used on hydrants or in pressure applications, as serious personal injury or death may occur.

ADDITIONAL ITEMS SUPPLIED WITH THE VEHICLE

- 1 - Pint of touch up paint for each color

- 1  -Bag of assorted stainless steel nuts and bolts

WHEEL CHOCKS

Two (2) ZICO #SAC-44 wheel chocks shall be mounted forward of the rear wheels on the driver side below the side running board compartments.

PAINT, PREPARATION AND FINISH

The PPG Delta, Low V.O.C., polyurethane finishing system, or equal, shall be utilized. A "Clear Coat" paint finish shall be supplied to provide greater protection to the quality of the exterior paint finish.

All removable items, such as brackets, compartment doors, etc. shall be painted separately to insure finish paint behind mounted items. All compartment unwelded seams exposed to high moisture environments shall be sealed using permanent pliable caulking prior to finish paint.

BODY PRIMER & PREPARATION

All exposed welds shall be ground smooth for final finishing of areas to be painted. The compartments and doors are totally degreased and phosphatized. After final body work is completed, grinding (36 and 80 grit), and finish sanding shall be used in preparation for priming.

BODY FINISH PAINT

The body shall be finish sanded and prepared for final paint. Upon completion of final preparation, the body shall be painted utilizing the highest quality, state of the art, low V.O.C., polyurethane base paint. Finish paint shall be applied in multiple coats to ensure proper paint coverage with a high gloss finish.

The entire body shall be buffed and detailed.

BODY PAINT

The inside and underside of the complete body assembly shall be painted job color prior to installation of the body on the chassis.

COMPARTMENT PAINT

The interior of the compartments shall be finish painted with Zolatone #20-63 Marble Stone scuff resistant paint to provide a protective application over all of the compartment interior surfaces.

BODY PAINT

The body paint finish shall be PPG Delta System, in a two tone configuration, to match customer furnished paint codes and requirements.

PUMP / PIPING PAINT

The pump enclosure and pump/plumbing within the pump enclosure shall be painted job color to match the primary color of the body.

CAB PRIMER & PREPARATION

The cab primer shall be a two (2) stage process. First stage shall be a coating with a two part component, self etching, and corrosion resistant primer to chemically bond the surface of the metal for increased adhesion. Second stage shall be multiple coats of a catalyzed, two component, polyurethane primer applied for leveling of small imperfections and top coat sealing.

CAB FINISH PAINT

The entire cab shall be finish sanded and prepared for final paint. Upon completion of final preparation, the cab shall be painted utilizing the highest quality, state of the art, low V.O.C., polyurethane base paint. Finish paint shall be applied in multiple coats to ensure proper paint coverage with a high gloss finish.

The cab exterior shall be painted with PPG Delta system to match purchaser's furnished paint codes. A two-tone paint finish shall be provided with the two-tone break line located approximately 3" below the cab side windows.

The entire exterior finish of the cab shall be buffed and detailed.

CAB INTERIOR PAINT

The interior metal surfaces of the cab shall be finish painted with a textured gray paint.

CHASSIS PAINT

The chassis frame rails, suspension and axles shall be painted black with a Polyurethane base paint prior to installation of any air lines or electric systems to ensure proper serviceability.

WHEEL PAINT

The chassis wheels, (except polished aluminum wheels) shall be painted job color with silver trim around the perimeter.

PAINT CODES

The paint shall match customer furnished paint code(s) and layout. The paint code(s) shall be as indicated below:

- PRIMARY PAINT COLOR

Single Color:	TBD	Paint Code#	TBD

- SECONDARY PAINT COLOR

Two/Tone Color:	TBD	Paint code#	TBD

TOUCH-UP PAINT

One (1) pint of each exterior color paint for touch-up purposes shall be supplied when the apparatus is delivered to the end user.

FINALIZATION & DETAILING

Prior to delivery the vehicle, the interior and exterior be cleaned and detailed. The finalization process detailing shall include installation of NFPA required labels, checking fluid levels, sealing and caulking required areas of the cab and body, rust proofing, paint touch-up, etc.

RUST PROOFING

The entire unit shall be thoroughly rust proofed utilizing rustproof and sound deadening materials applied in manufacturer recommended application procedures. Rust proofing shall be applied during the assembly process and upon completion to insure proper coverage in all critical areas.

COMPUTER GENERATED LETTERING

The lettering and striping shall be custom designed utilizing state of the art computer software and computerized cutting machines. The manufacturer shall employ a full time artist / designer to generate all lettering, decals, and striping to meet the requirements of the Fire Department. The artwork for the lettering and striping shall be kept on record by the apparatus manufacturer to allow for ease in duplication for the Fire Department.

FRONT CAB DOOR LETTERING

Scotch-Lite with drop shadow lettering shall be provided on the cab driver's and officer's doors per the fire department requirements. The design of the lettering on the cab doors shall be designed to fit in the 496 sq. inches available.

Lettering provided on the driver's and officer's cab doors shall be 4" high.

REAR CAB DOOR LETTERING

Scotch-Lite with drop shadow lettering shall be provided on the cab crew doors per the fire department requirements. The design of the lettering on the cab doors shall be designed to fit in the 496 sq. inches available.

Lettering provided on the crew cab doors shall be 4" high.

CAB GRILL OR BUMPER LETTERING

Scotch-Lite with drop shadow lettering shall be provided on the front of the cab per the fire department requirements. The design of the lettering on the front of the cab shall be designed to fit in the 167 sq. inches available.

Lettering provided on the front of cab shall be 4" high.

LETTERING FONT

The lettering shall be designed and cut with a basic block type font:

"BLOCK TYPE FONT"

STANDARD MALTESE CROSS DESIGN 1

A pair of standard Maltese crosses shall be computer generated and will be no larger than the 496 sq. inches available.

The standard logo shall be printed on Scotch-Lite with two computer generated printed colors.

The Maltese cross shall be located as directed by the Fire Department.

SCOTCH-LITE STRIPE

A six (6) inch high "Scotch-Lite" stripe shall be provided. The stripe shall be applied on a minimum of 60 percent of each side of the unit, 60 percent on the rear of the unit and 40 percent on the front of the unit. The Scotch-Lite stripe layout shall be determined by the Fire Department.

The Scotch-Lite shall be white in color.

SCOTCH-LITE ACCENT STRIPES

A 1" high Scotch-Lite material accent stripe shall be incorporated into the Scotch-Lite scheme to border the primary Scotch-Lite stripe on the top and bottom edges. Final layout of this configuration shall be determined by the Fire Department.

REAR CHEVRON STRIPING

At least 50% of the rear facing vertical surface shall be covered with alternating strips of reflective striping.

The striping shall be 6" ScotchLite.

The Scotch-Lite shall be Red and Yellow in color.

VEHICLE WARRANTY

The proposed vehicle includes a one (1) year new vehicle warranty, upon delivery and acceptance of the vehicle. The warranty will ensure that the vehicle has been manufactured to the proposed contract specifications and will be free from defects in material and workmanship that may appear under normal use and service within the warranty period. The warranty may be subject to different time and mileage limitations for specific components and parts. This warranty is issued to the original purchaser of the vehicle.

The warranty will not apply to tires, batteries, or other parts or components that are warranted directly by their manufacturers. The warranty will not apply to routine maintenance requirements as described in the service and operator's manual. No warranty whether express, implied, statutory or otherwise including, but not limited to any warranty of merchantability or fitness for purpose will be imposed.

OVERALL UNIT AND CUSTOM CHASSIS

All components and parts of the vehicle are warranted for a period of one (1) year from acceptance of the vehicle, unless excluded elsewhere in this warranty or described as having longer time limitations.

ENGINE WARRANTY

The unit will be equipped with a Fire Service rated engine, which will come furnished with a five (5) year Engine Manufacturer's warranty. A copy of the manufacturer's warranty will be supplied to define additional details of the warranty provisions.

TRANSMISSION WARRANTY

The required Allison transmission shall be provided with a five (5) year warranty. A copy of the Allison transmission warranty shall be supplied to the purchaser to define additional details of the warranty provisions.

CUSTOM CHASSIS FRAME RAILS

The proposed KME custom chassis frame and cross members will be warranted for an unlimited time period. A copy of KME's frame rail warranty will be supplied to define additional details of the warranty provisions.

CROSSMEMBERS WARRANTY

A lifetime warranty will be provided on all chassis frame crossmembers.

MERITOR AXLE WARRANTY

The Meritor axle/s will be provided with a two (2) year parts and labor warranty. The wheel seals, gaskets and wheel bearings will have a one (1) year warranty. A copy of Meritor's warranty will be supplied to define additional details of the warranty provisions.

CAB STRUCTURE WARRANTY

The proposed cab will be warranted against structural defects for a period of ten (10) years from the date of acceptance of the unit. Details of warranty coverage, limitations and exclusions are included in the specific warranty document.

BODY STRUCTURE WARRANTY

The proposed body will be warranted against structural defects for a period of ten (10) years from the date of acceptance of the unit. Details of warranty coverage, limitations and exclusions are included in the specific warranty document.

CORROSION WARRANTY

The proposed cab and body will be warranted against rust-through or perforation, due to corrosion from within, for a period of ten (10) years. Perforation is defined as a condition in which an actual hole occurs in a sheet metal panel due to rust or corrosion from within. Surface rust or corrosion caused by chips or scratches in the paint is not covered by this warranty.

PAINT FINISH WARRANTY

The paint finish will be warranted for a period of seven (7) years from the date of acceptance of the unit. Details of warranty coverage, limitations and exclusions are included in the specific warranty document.

STAINLESS STEEL PLUMBING WARRANTY

The proposed stainless steel plumbing will be warranted for a period of ten (10) years from the date of acceptance of the unit. Details of warranty coverage, limitations and exclusions are included in the specific warranty document.

WATER TANK (LIFETIME)

The proposed water tank will be warranted by the water tank manufacturer for the "Lifetime" of the unit. A copy of the manufacturer's warranty will be supplied to define additional details of the warranty provisions.

WATEROUS FIRE PUMP (FIVE YEAR LIMITED)

Waterous warrants, to the original Buyer only, that products manufactured by Waterous will be free from defects in material and workmanship under normal use and service for a period of five (5) years from the date the product is first placed in service or five and one-half (5 1/2) years from the date of shipment by Waterous, whichever period shall be the first to expire; provided the buyer notifies Waterous, in writing, of the defect in said product within the warranty period, and said product is found by Waterous to be nonconforming with the aforesaid warranty.